## Slide 1: Activity Two
Kernel Modules with eSDKs
Marco Cavallini

## Slide 2: Kernel modules with eSDKs – Overview
The Extensible SDK (eSDK) is a portable and standalone development environment , basically an SDK with an added bitbake executive via devtool.
The “devtool” is a collection of tools to help development, in particular user space development.
We can use devtool to manage a new kernel module:
  Like normal applications is possible to import and create a wrapper recipe to manage the kernel module with eSDKs.

## Slide 3: Kernel modules with eSDKs – Compiling a kernel module
We have two choices
Out of the kernel tree
  When the code is in a different directory outside of the kernel source tree
Inside the kernel tree
  When the code is managed by a KConfig and a Makefile into a kernel directory

## Slide 4: Kernel modules with eSDKs – Pro and Cons of a module outside the kernel tree
When the code is outside of the kernel source tree in a different directory
Advantages
  Might be easier to handle modifications than modify it into the kernel itself
Drawbacks
  Not integrated to the kernel configuration/compilation process
  Needs to be built separately
  The driver cannot be built statically

## Slide 5: Kernel modules with eSDKs – Pro and Cons of a module inside the kernel tree
When the code is inside the same directory tree of the kernel sources
Advantages
  Well integrated into the kernel configuration and compilation process
  The driver can be built statically if needed
Drawbacks
  Bigger kernel size
  Slower boot time

## Slide 6: Kernel modules with eSDKs – The source code
#include <linux/module.h>
#include <linux/kernel.h>
static int __init hello_init(void)
{
printk("When half way through the journey of our life\n");
return 0;
}
static void __exit hello_exit(void)
{
printk("I found that I was in a gloomy wood\n");
}
module_init(hello_init);
module_exit(hello_exit);
MODULE_LICENSE("GPL");
MODULE_DESCRIPTION("Greeting module from the Divine Comedy");
MODULE_AUTHOR("Dante Alighieri");

## Slide 7: Kernel modules with eSDKs – The Makefile
obj-m += hellokernel.o SRC := $(shell pwd) all: $(MAKE) -C $(KERNEL_SRC) M=$(SRC) modules modules_install: $(MAKE) -C $(KERNEL_SRC) M=$(SRC) modules_install
KERNEL_SRC is the location of the kernel sources.
This variable is set to the value of the STAGING_KERNEL_DIR within the module class (module.bbclass)
Sources available on https://github.com/koansoftware/simplest-kernel-module.git
Notes: Note in do_install, the ‘/’ is NOT missing between ${D}${bindir}
We cd ${S} because default is ${B}, no source in ${B} (not default same as ${S} anymore)

## Slide 8: Kernel modules with eSDKs – Devtool setup
Start a new Shell! Otherwise, the existing bitbake environment can cause unexpected results
Here is how the eSDK was prepared for this class account:
This installed the eSDK into: /scratch/sdk/qemuarm
< DO NOT ENTER THE FOLLOWING COMMANDS : ALREADY EXECUTED >
$ bitbake core-image-base -c populate_sdk_ext
$ cd /scratch/working/build-qemuarm/tmp/deploy/sdk/
$ ./poky-glibc-x86_64-core-image-base-armv5e-toolchain-ext-2.4.sh \
-d /scratch/sdk/qemuarm –y
$ cd /scratch/sdk/qemuarm
$ . environment-setup-armv5e-poky-linux-gnueabi
$ devtool modify virtual/kernel
$

## Slide 9: Kernel modules with eSDKs – Overview
Starting from now we are using the eSDK and not the project
During this exercise we using two different machines
  The HOST containing the eSDK (providing devtool)
  The TARGET running the final qemuarm image
Host
eSDK:~$
Target
root@qemuarm:~$

## Slide 10: Kernel modules with eSDKs – Globalsetup
Open two terminal windows and setup the eSDK environment in each one
$ cd /scratch/sdk/qemuarm
$ bash # safe shell
$ source environment-setup-armv5e-poky-linux-gnueabi
…
SDK environment now set up;
additionally you may now run devtool to perform development tasks.
Run devtool --help for further details.
$

## Slide 11: Kernel modules with eSDKs – build the target image
After you have setup the eSDK environment, build an image
This will create a new image into: /scratch/sdk/qemuarm/tmp/deploy/images/qemuarm
$ devtool build-image

## Slide 12: Kernel modules with eSDKs – build the target image
Run the image to check if everything is OK
This will run the QEMU machine in the TARGET shell you were using
Login using user: root (no password required)
$ runqemu qemuarm nographic

## Slide 13: Kernel modules with eSDKs – Hooking a new module into the build
Run the devtool to add a new recipe (on the HOST side)
  This generates a minimal recipe in the workspace layer
  This adds EXTERNALSRC in an workspace/appends/simplestmodule_git.bbappend file that points to the sources
  In other words, the source tree stays where it is, devtool just creates a wrapper recipe that points to it
Note: this does not add your image to the original build engineer’s image, which requires changing the platform project’s conf/local.conf
$ devtool add --version 1.0 simplestmodule \
/scratch/src/kmod/simplest-kernel-module/

## Slide 14: After the add
Workspace layer layout
$ tree /scratch/sdk/qemuarm/workspace/ /scratch/sdk/qemuarm/workspace/ ├── appends │ └── simplestmodule_git.bbappend ├── conf │ └── layer.conf ├── README └── recipes └── simplestmodule └── simplestmodule_git.bb
Notes: The build directory

## Slide 15: Kernel modules with eSDKs – Build the Module
Build the new recipe (on the HOST side)
This will create the simplestmodule.ko kernel module
This downloads the kernel sources (already downloaded for you): linux-yocto-4.12.12+gitAUTOINC+eda4d18ce4_67b62d8d7b-r0 do_fetch
$ devtool build simplestmodule

## Slide 16: Kernel modules with eSDKs – Deploy the Module
Get the target’s IP address from the target serial console root@qemuarm:~# ifconfig
In the eSDK (HOST) shell, deploy the output (the target’s ip address may change)
NOTE: the ‘-s’ option will note any ssh keygen issues, allowing you to (for example) remove/add this IP address to the known hosts table
$ devtool deploy-target -s simplestmodule root@192.168.7.2

## Slide 17: Kernel modules with eSDKs – Deploy Details
In the target (qemuarm), observe the result of deployment
devtool_deploy.list 100% 108 0.1KB/s 00:00
devtool_deploy.sh 100% 1017 1.0KB/s 00:00
./
./lib/
./lib/modules/
./lib/modules/4.12.12-yocto-standard/
./lib/modules/4.12.12-yocto-standard/extra/
./lib/modules/4.12.12-yocto-standard/extra/hellokernel.ko
./usr/
./usr/include/
./usr/include/simplestmodule/
./usr/include/simplestmodule/Module.symvers
./etc/
./etc/modprobe.d/
./etc/modules-load.d/
NOTE: Successfully deployed
/scratch/sdk/qemuarm/tmp/work/qemuarm-poky-linux-gnueabi/simplestmodule/

## Slide 18: Kernel modules with eSDKs – Load the Module
In the target (qemuarm), load the module and observe the results
root@qemuarm:~# depmod –a
root@qemuarm:~# modprobe hellokernel
[ 874.941880] hellokernel: loading out-of-tree module taints kernel.
[ 874.960165] When half way through the journey of our life
root@qemuarm:~# lsmod
Module Size Used by
hellokernel 929 0
nfsd 271348 11

## Slide 19: Kernel modules with eSDKs – Unload the Module
In the target (qemuarm), unload the module
root@qemuarm:~# modprobe -r hellokernel
[ 36.005902] I found that I was in a gloomy wood
root@qemuarm:~# lsmod
Module Size Used by
nfsd 271348 11

## Slide 20: Kernel modules with eSDKs – automatic load of the module at boot
In the target (qemuarm), edit the file below and add a new line containing the module name ‘hellokernel’
Then reboot the Qemu machine and verify
root@qemuarm:~# vi /etc/modules-load.d/hello.conf
< insert the following line and save >
hellokernel
root@qemuarm:~# reboot

## Slide 21
Questions