## Slide 1: Advanced Class
Paul Barker, Marco Cavallini, Beth Flanagan, Sean Hudson, Joshua Lock, Scott Murray, Tim Orling, David Reyna, Rudi Streif, Marek Vasut
Yocto Project Developer Day  Prague 26 October 2017

## Slide 2: Advanced Class
Class Content:
  https://wiki.yoctoproject.org/wiki/DevDay_Prague_2017
Requirements:
  Wireless
  SSH (Windows: e.g. “putty”)
  Serial (Linux: “screen”, Windows: e.g. “Teraterm”)
Wireless Registration:
  TBD

## Slide 3: Agenda – The Advanced Class
9:00- 9:15 Opening session, What's New (Jefro)
9:15- 9:30 Account setup (David Reyna)
9:30-10:15 Devtool: creating new content (Tim Orling)
10:15-10:30 Morning Break
10:30-11:15 DT overlays (Marek Vasut)
11:15-12:00 Userspace: packaging, installation, system services (Rudolf Streif, given by David Reyna)
12:00- 1:00 Lunch (and board pass-out)
1:00- 1:45 License audit of a release (Beth 'pidge' Flanagan)
1:45- 2:15 CROPS (Tim Orling)
2:30- 2:45 Afternoon Break
2:45- 3:15 Recipe specific sysroots (Joshua Lock, given by Sean Hudson)
3:15- 3:45 Maintaining your Yocto Distribution (Scott Murray)
3:45- 4:20 Kernel Modules with eSDKs (Marco Cavallini)
4:20- 5:00 Analytics and the Event System (David Reyna)
5:00- 5:30 Kernel/Security Forum, Q and A (All)

## Slide 4: Activity One
Class Account Setup

## Slide 5: Notes for the Advanced Class:
The class will be given with YP-2.4 (Rocko)
Wifi Access:
  SSID: <TBD>
  Password: <TBD>
Your account’s IP access addresses
  SSH (password “devday”):
      ssh ilab01@devday-a.yocto.io -p 10000(+your session number)
  HTTP: http://devday-a.yocto.io:30000(+your session number)

## Slide 6: Yocto Project Dev Day Lab Setup
The virtual host’s resources can be found here:
  Your Project: "/scratch/working/build-arm“
  Extensible-SDK Install: "/scratch/sdk/arm“
  Sources: "/scratch/src“
  Poky: "/scratch/poky"
  Downloads: "/scratch/downloads"
  Sstate-cache: "/scratch/sstate-cache"
  QEMU/Toaster Install: "/scratch/build“
You will be using SSH to communicate with your virtual server.
You may want to change the default password (“devday”) after you log on, in case someone accidently uses the same account address as yours.

## Slide 7: FYI: How class project was prepared
$ cd /scratch
$ git clone -b rocko git://git.yoctoproject.org/poky.git
$ cd poky
$ ./scratch/poky/oe-init-build-env build
$ echo "MACHINE = \“qemuarm\"" >> conf/local.conf
$ echo "SSTATE_DIR = \“/scratch/sstate-cache\"" >> conf/local.conf
$ echo "DL_DIR = \“/scratch/downloads\"" >> conf/local.conf
$ echo "IMAGE_INSTALL_append = \" gdbserver openssh libstdc++ \
curl \"" >> conf/local.conf
$ # Capture the build into a Bitbake/Toaster database
$ . toaster start webport=0.0.0.0:8000
$ # Build the project
$ bitbake core-image-base
$ # Prepare eSDK
$ bitbake core-image-base -c populate_sdk_ext
$ cd /scratch/sdk
$ /scratch/poky/build/tmp/deploy/sdk/poky-glibc-*-toolchain-ext-*.sh \
–d `pwd` -y
$. environment-setup-armv5e-poky-linux-gnueab
$ devtool build-image

## Slide 8: NOTE: Clean Shells!
We are going to do a lot of different exercises in different build projects, each with their own environments.
To keep things sane, you should have a new clean shell for each exercise.
There are two simple ways to do it:
  Close your existing SSH connection and open a new one -- or –
  Do a “bash” before each exercise to get a new sub-shell, and “exit” at the end to remove it, in order to return to a pristine state.

## Slide 9: Activity Two
Devtool
Tim Orling

## Slide 10: Activity Three
DT overlays
Marek Vasut

## Slide 11
Device Tree
Data structure describing hardware
Tree with cycles
Example:
/dts-v1/;
#include <dt-bindings/interrupt-controller/arm-gic.h>
/ {
model = "V2F-1XV7 Cortex-A53x2 SMM";
arm,hbi = <0x247>;
[...]
chosen {
stdout-path = "serial0:38400n8";
};
[...]
gic: interrupt-controller@2c001000 {
interrupt-controller;
reg = <0 0x2c001000 0 0x1000>,
<0 0x2c002000 0 0x2000>,
[...]

## Slide 12
Problem – Variable hardware
DT started on machines the size of little fridge
  HW was mostly static
  DT was baked into PROM, optionally modified by bootloader
DT was good, so it spread
  First PPC, embedded PPC, then ARM …
There always was slightly variable hardware
  Solved by patching DT in bootloader
  Solved by carrying multiple DTs
  Solved by co-operation of board files and DT
  ^ all that does not scale

## Slide 13
Problem – Variable hardware – 201x edition
Come 201x, variable HW became easy to make:
  Cheap devkits with hats, lures, capes, …
  FPGAs and SoC+FPGAs became commonplace …
  => Combinatorial explosion of possible HW configurations
Solution retaining developers’ sanity
  Describe only the piece of HW that is being added
  Combine these descriptions to create a DT for the system
  Enter DT overlays

## Slide 14
Device Tree Overlays
DT: Data structure describing hardware
DTO: necessary change(s) to the DT to support particular feature
  Example: an expansion board, a hardware quirk,...
Example DTO:
/dts-v1/;
/plugin/;
/ {
#address-cells = <1>;
#size-cells = <0>;
fragment@0 {
reg = <0>;
target-path = "/";
__overlay__ {
#address-cells = <1>;
#size-cells = <0>;
hello@0 {
compatible = "hello,dto";
reg = <0>;
}; }; }; };

## Slide 15
Advanced DTO example
/dts-v1/;
/plugin/;
[...]
fragment@2 {
reg = <2>;
target-path = "/soc/usb@ffb40000";
__overlay__ {
[...]
status = "okay";
};
};
fragment@3 {
reg = <3>;
target-path = "/soc/ethernet@ff700000";
__overlay__ {
[...]
status = "okay";
phy-mode = "gmii";
};
};

## Slide 16
DTO Hands-on
Use pre-prepared meta-dto-microdemo layer
meta-dto-demo contains:
    Kernel patch with DTO loader with ConfigFS interface
    Kernel config fragment to enable the DTO and loader
    Demo module
    Demo DTO source ( hello-dto.dts )
    core-image-dto-microdemo derivative from core-image-minimal with added DTO examples and DTC

## Slide 17
DTO Hands-on 1/2
Add meta-dto-demo to bblayers.conf BBLAYERS:
Rebuild virtual/kernel and core-image-dto-microdemo
Start the new image in QEMU
$ ${EDITOR} conf/bblayers.conf
$ bitbake -c cleansstate virtual/kernel
$ bitbake core-image-dto-microdemo
$ runqemu qemuarm

## Slide 18
DTO Hands-on 2/2
Compile DTO
Load DTO
Unload DTO
$ dtc -I dts -O dtb /lib/firmware/dto/hello-dto.dts > \
/tmp/hello-dto.dtb
$ mkdir /sys/kernel/config/device-tree/overlays/mydto
$ cat /tmp/hello-dto.dtb > \
/sys/kernel/config/device-tree/overlays/mydto/dtbo
$ rmdir /sys/kernel/config/device-tree/overlays/mydto

## Slide 19
DTO encore
DTOs can be used to operate SoC+FPGA hardware
Done using FPGA manager in Linux
fragment@0 {
reg = <0>;
/* controlling bridge */
target-path = "/soc/fpgamgr@ff706000/bridge@0";
__overlay__ {
#address-cells = <1>;
#size-cells = <1>;
area@0 {
compatible = "fpga-area";
#address-cells = <2>;
#size-cells = <1>;
ranges = <0 0x00000000 0xff200000 0x00080000>;
firmware-name = "fpga/bitstream.rbf";
fpga_version@0 {
compatible = "vendor,fpgablock-1.0";
reg = <0 0x0 0x04>;
};

## Slide 20: Activity Four
Userspace: Advanced Topics
Rudi Streif
(given by David Reyna)

## Slide 21: What We Are Going To Do
Most of your development work will likely be developing your own software packages, building them with the Yocto Project and installing them into a root file system built with the Yocto Project.
Let’s look at some typical tasks beyond creating the base recipe:
  Customizing Packaging
  Package Installation Scripts
  System Services

## Slide 22: Activity Setup
Initialize the Build Environment (IN A CLEAN SHELL)
  cd /scratch/working
  source ../poky/oe-init-build-env build-userspace
Adjust Configuration (DONE FOR YOU)
  vi conf/local.conf
Build (DONE FOR YOU)
  bitbake -k core-image-base
Test
  runqemu qemux86-64 nographic
MACHINE = "qemuarm"
DL_DIR ?= "/scratch/downloads"
SSTATE_DIR ?= "/scratch/sstate-cache"
EXTRA_IMAGE_FEATURES ?= "debug-tweaks dbg-pkgs dev-pkgs package-management"

## Slide 23: Activity Setup - Continued
Create Layer
  devtool create-workspace meta-uspapps
Copy Source Files
  cd ..
  cp -r /scratch/src/userspace/uspsrc .

## Slide 24: Packaging
Packaging is the process of putting artifacts from the build output into one or more packages for installation by a package management system.
Packaging is performed by the package management classes:
  package_rpm – RPM style packages
  package_deb – Debian style packages
  package_ipk – IPK package files used by the OPK package manager
You configure the package management in conf/local.conf:
  You can add more than one of the package classes.
  Only the first one will be used to create the root file system.
  However, this does not install the package manager itself.
Install the package manager in conf/local.conf:
PACKAGE_CLASSES ?= "package_rpm"
EXTRA_IMAGE_FEATURES ?= "package-management"

## Slide 25: Package Splitting
Packaging Splitting is the process of putting artifacts from the build output into different packages.
Package splitting allows you to select what you need to control the footprint of your root file system.
Package splitting is controlled by the variables:
  PACKAGES – list of package names, default:
  FILES – list of directories and files that belong into the package:
PACKAGES = "${PN}-dbg ${PN}-staticdev ${PN}-dev ${PN}-doc \ ${PN}-locale ${PACKAGE_BEFORE_PN} ${PN}"
SOLIBS = "*.so.*“ FILES_${PN} = "${bindir}/* ${sbindir}/* ${libexecdir}/* \ ${libdir}/lib* {SOLIBS} ${sysconfdir} ${sharedstatedir} \ ${localstatedir} ${base_bindir}/* ${base_sbindir}/* \ ${base_libdir}/*${SOLIBS} ${base_prefix}/lib/udev/rules.d \ ${prefix}/lib/udev/rules.d ${datadir}/${BPN}\ ${libdir}/${BPN}/* ${datadir}/pixmaps \ ${datadir}/applications ${datadir}/idl ${datadir}/omf \ ${datadir}/sounds ${libdir}/bonobo/servers"

## Slide 26: Package Splitting - Continued
The package classes process the PACKAGES list from left to right, producing the ${PN}-dbg package first and the ${PN} package last.
The order is important, since a package consumes the files that are associated with it.
The ${PN} package is pretty much the “kitchen sink”: it consumes all standard leftover artifacts.
BitBake syntax only allows prepending (+=) or appending (=+) to variables:
  Prepend PACKAGES – place standard artifacts into different packages
  Append PACKAGES – place any leftover packages in non-standard installation directories those packages.
The variable PACKAGE_BEFORE_PN allows you to insert packages right before the ${PN} package is created.

## Slide 27: Packaging QA
The insane class adds plausibility and error checking to the packaging process.
You can find a list of the checks in the Reference Manual: http://www.yoctoproject.org/docs/2.3/ref-manual/ref-manual.html#ref-classes-insane
Some of the more common ones:
  already-stripped – debug symbols already stripped
  installed-vs-shipped – checks for artifacts that have not been packaged
  ldflags – checks if LDFLAGS for cross-linking has been passed
  packages-list – same package has been listed multiple times in PACKAGES
Sometimes the checks can get into your way…
  INSANE_SKIP_<packagename> += “<check>”
  Skips <check> for <packagename>.

## Slide 28: Example – The Fibonacci Library
Source code in /scratch/working/uspsrc/fibonacci-lib
  Builds static and dynamic libraries to calculate the Fibonacci series and an application to test it.
Create development environment
  cd /scratch/working/build-userspace
  devtool add fibonacci-lib /scratch/working/uspsrc/fibonacci-lib
Build the recipe
  bitbake fibonacci-lib
Add to your image (conf/local.conf):
Build and test image
  bitbake core-image-minimal
  runqemu qemux86-64 nographic
IMAGE_INSTALL_append = " fibonacci"

## Slide 29: Example – The Fibonacci Library (continued)
Edit the recipe meta-uspapps/recipes/fibonacci-lib/fibonacci-lib.bb and place the fibonacci test application into its own package ${PN}-examples
Add to your image (conf/local.conf):
Build and test image
  bitbake core-image-minimal
  runqemu qemux86-64 nographic
PACKAGE_BEFORE_PN = "${PN}-examples" FILES_${PN}-examples = "${bindir}/fibonacci"
IMAGE_INSTALL_append = " libfibonacci libfibonacci-examples"

## Slide 30: Package Installation Scripts
Package management systems have the ability to run scripts before and after a package is installed, upgraded, or removed.
These are typically shell scripts and they can be provided by the recipe using these variables:
  pkg_preinst_<packagename>: Preinstallation script that is run before the package is installed.
  pkg_postinst_<packagename>: Postinstallation script that is run after the package is installed.
  pkg_prerm_<packagename>: Pre-uninstallation script that is run before the package is uninstalled.
  pkg_postrm_<packagename>: Post-uninstallation script that is run after the package is uninstalled.
pkg_postinst_${PN}() {
#!/bin/sh
# shell commands go here
}
pkg_postinst_${PN}() {
#!/bin/sh
if [ x"$D" = "x" ]; then
# target execution
else
# build system execution
fi
}
Conditional Execution
Script Skeleton

## Slide 31: Example – Conditionally running ldconfig
The Fibonacci library installs a dynamic library libfibonacci.so.1.0 on the target system in /usr/lib.
For ld to be able to locate the library it must be added to the ld cache and its symbolic name (soname) must be linked. That is done by running ldconfig on the target.
Add a post installation script to the ${PN} package that only runs ldconfig when it is run on the target but not when the build system creates the root file system.
pkg_postinst_${PN}() {
#!/bin/sh
if [ x"$D" = "x" ]; then
# target execution ldconfig
exit 0
else
# build system execution
exit 1
fi
}

## Slide 32: Installation for Packaging
Makefile Installation
Recipe Installation
  Providing/overriding the do_install task
  The build system defines a series of variables for convenience:
      bindir = "/usr/bin"
      sbindir = "/usr/sbin"
      libdir = "/usr/lib"
      libexecdir = "/usr/lib"
do_install() {
install –d ${D}${bindir} install –m 0755 ${B}/bin/* ${D}{bindir}
}
  sysconfdir = "/etc/"
  datadir = "/usr/share"
  mandir = "/use/share/man"
  includedir = "/usr/include"
INSTALL ?= install
.PHONY: install
Install:
$(INSTALL) -d $(DESTDIR)/usr/bin
$(INSTALL) -m 0755 $(TARGET) $(DESTDIR)/usr/bin

## Slide 33: Debugging Packaging
Check the packaging logfiles in ${WORKDIR}/temp
Check installation of artifacts in ${WORKDIR}/image
  The do_install task installs the artifacts into this directory.
  If artifacts are missing they are packaged.
Check packaging artifacts in ${WORKDIR}/package
  This where the artifacts are staged for packaging, including the ones created for the debug packages.
Check package splitting in ${WORKDIR}/packages-split
  Packages and their content are staged here by package name before they are wrapped by the package manager.
  Allows you to verify if the artifacts have indeed been placed into the correct package.
Check created packages in ${WORKDIR}/deploy-<pkgmgr>

## Slide 34: Package Architecture
The build system distinguishes packages by their hardware dependencies into three main categories:
  Tune – Generic CPU architecture such as core2_32, corei7, armv7, etc. This is the default and typically appropriate for userspace packages.
  Machine – Specific machine architecture. Appropriate for packages that require particular hardware features of a machine. Typically applicable to kernel, drivers, and bootloader.
  All – Package applies to all architectures such as shell scripts, managed runtime code (Python, Lua, Java, …), configuration files, etc.
Package architecture is controlled by the PACKAGE_ARCH variable:
  Tune (default) – PACKAGE_ARCH = “${TUNE_PKGARCH}”
  Machine – PACKAGE_ARCH = “${MACHINE_ARCH}”
  All – inherit allarch
Note: Package architecture does not simply determine into what category a package is placed but determines compiler and linker flags and other build options.

## Slide 35: System Services
If your software package is a system service that eventually needs to be started when the system boots you need to add the scripts and service files.
SysVInit
  Inherit update-rc.d class.
  INITSCRIPT_PACKAGES - List of packages that contain the init scripts for this software package. This variable is optional and defaults to INITSCRIPT_PACKAGES = "${PN}".
  INITSCRIPT_NAME - The name of the init script.
  INITSCRIPT_PARAMS - The parameters passed to update-rc.d. This can be a string such as "defaults 80 20" to start the service when entering run levels 2, 3, 4, and 5 and stop it from entering run levels 0, 1, and 6.
Systemd
  Inherit systemd class.
  SYSTEMD_PACKAGES - List of packages that contain the systemd service files for the software package. This variable is optional and defaults to SYSTEMD_PACKAGES = "${PN}".
  SYSTEMD_SERVICE - The name of the service file.

## Slide 36: Example – The Fibonacci Server
Source code in /scratch/working/uspsrc/fibonacci-srv
  Builds a TCP socket server listening on port 9999 for the number of terms and responds with the list of Fibonacci terms.
Create development environment
  cd /scratch/working/build-userspace
  devtool add fibonacci-srv /scratch/working/uspsrc/fibonacci-srv
Add system service startup to the recipe meta-uspapps/recipes/fibonacci-srv/fibonacci-srv.bb
Build the recipe
  bitbake fibonacci-lib
Add to your image (conf/local.conf):
Build and test image
  bitbake core-image-minimal
  runqemu qemux86-64 nographic
  nc localhost 9999
IMAGE_INSTALL_append = " fibonacci-srv"
inherit update-rc.d systemd
INITSCRIPT_NAME = "fibonacci-srv"
INITSCRIPT_PARAMS = "start 99 3 5 . stop 20 0 1 2 6 ."
SYSTEMD_SERVICE = "fibonacci-srv.service"

## Slide 37: Changing the System Manager
SysVInit is the default system manager for the Poky distribution.
To use systemd add it to your conf/local.conf file, or better, to your distribution configuration:
If you exclusively want to use systemd, you can remove SysVInit from you root file system image with:
DISTRO_FEATURES_append = " systemd"
VIRTUAL-RUNTIME_init_manager = "systemd"
DISTRO_FEATURES_BACKFILL_CONSIDERED = "sysvinit"
VIRTUAL-RUNTIME_initscripts = ""

## Slide 38: Activity Five
License audit of a release
Beth 'pidge' Flanagan, Paul Barker

## Slide 39: Activity Six
CROPS
Tim Orling

## Slide 40: Activity Seven
Recipe Specific Sysroots
Joshua Lock
(given by Sean Hudson)

## Slide 41: Recipe Specific Sysroots - Overview
Topics
  Definitions
  Determinism improvements in YP 2.3 +
  Future reproducibility work

## Slide 42: Recipe Specific Sysroots
Reproducible
  Repeatable: rerun a build and have it succeed (or fail) in the same way
  Deterministic: given the same inputs the build system should produce equivalent outputs
  Binary reproducible: given the same inputs the system should produce bit-for-bit identical outputs

## Slide 43: Recipe Specific Sysroots
Reproducibility and Yocto Project
Repeatability was a founding goal of the Yocto Project
  Not as common place at the time of the project’s inception
Determinism of the YP build system has improved over time
  Vast leap forward with most recent, Pyro, release
Being able to build binary reproducible artefacts is a goal for future development
  Some concrete tasks planned for 2.4

## Slide 44: Recipe Specific Sysroots
Binary Reproducible
Fully deterministic build system, producing bit-for-bit identical output given the same inputs
Build environment is recorded or pre-defined
Mechanism for users to:
  Recreate the environment
  Repeat the build
  Verify the output matches
https://reproducible-builds.org/

## Slide 45: Recipe Specific Sysroots
Yocto Project Reproducibility Features
DL_DIR – shareable cache of downloads
Easily replicated build environment - configuration in known locations, printed build header
Shared state mechanism – reusable intermediary objects when inputs haven’t changed
SSTATE_MIRRORS – remotely addressable cache of shared state objects
Uninative – static libc implementation for use with native tools, improves sstate reuse
Fixed locale – ensures consistent date/time format, sort order, etc

## Slide 46: Recipe Specific Sysroots
Topics
  Definitions
  Determinism improvements in YP 2.3 +
  Future reproducibility work

## Slide 47: Recipe Specific Sysroots
Shared sysroots – a long-standing source of non-determinism
Shared sysroot used by YP build system until 2.3/Pyro release
Cause of non-determinism, particularly with long-lived workspaces
  automatic detection of items in the sysroot which weren't explicitly marked as a dependency
  items which appear lower in common YP build graphs such as libc, kernel or common native dependencies such as glib-2.0-native

## Slide 48: Recipe Specific Sysroots
Recipe specific sysroots improve determinism
per-recipe sysroot which only includes sysroot components of explicit dependencies
sysroot artefacts are installed into a component specific location
built by hard-linking dependencies files in from their component trees
reinstall sysroot content when the task checksum of the dependency changes
resolves the issue of autodetected dependencies and implicit dependencies through build order

## Slide 49: Recipe Specific Sysroots
Implementations challenges
Artefacts in the component sysroots can include hard-coded paths – we need to be able to fix them for installed location
  The code knows to look at certain common sites for hard-coded paths and can be taught to fixup in more locations by appending to the EXTRA_STAGING_FIXMES variable
A recipe is composed of several tasks to run in the course of building its output; fetch, unpack, configure, etc.
  Many of these tasks have task-specific dependencies, we need to re-extend the sysroot when tasks explicitly require items in the sysroot. i.e. do_package_write_deb need dpkg-native do_fetch for a git repo requires git-native

## Slide 50: Recipe Specific Sysroots
Implementations challenges (II)
post-install scriptlets need to be executed for each recipe-specific sysroot
  We handle this by installing postinst scriptlets into the recipe-specifc sysroot with a postinst- prefix and running all of the scriptlets as part of the sysroot setup
Still need to be able to replicate old shared-sysroot behaviour in certain scenarios, i.e. eSDK
  bitbake build-sysroot recipe target takes everything in the components directory which matches the current MACHINE and installs it into a shared sysroot

## Slide 51: Recipe Specific Sysroots
Adapting to recipe specific sysroots
Would have liked to be pain-free transition, but there is some conversion required for recipe-specific sysroots.
fix missing dependencies – commonly native dependencies, i.e. glib-2.0-native
SSTATEPOSTINSTFUNCS → SYSROOT_PREPROCESS_FUNCS
  SSTATEPOSTINSTFUNCS are a hook to call specific functions after a recipe is populated from shared state, commonly used for fixing up paths.
  As shared state objects will now be installed into the recipe-component location, then linked into the recipe specific sysroot, we need to be able to perform such fixes in each constructed sysroot.
  SYSROOT_PREPROCESS_FUNCS: is list of functions to run after sysroot contents are staged and the right place to perform relocation in RSS world

## Slide 52: Recipe Specific Sysroots
Adapting to recipe specific sysroots (II)
Add PACKAGE_WRITE_DEPS for any postinsts requiring native tools at rootfs construction
  YP build system tries to run preinst and postinsts at rootfs construction time, deferring any which fail to first boot.
  Any special native tool dependencies of pkg_preinst and pkg_postinst must be explicitly listed in PACKAGE_WRITE_DEPS to ensure they are available on the build host at rootfs construction time.

## Slide 53: Recipe Specific Sysroots
Unexpected consequences
Recipe specific sysroots aggravated an existing source of non-determinism
PATH included locations in the host for boot-strapping purposes
Host tools were being used, where available, when native dependencies were missing

## Slide 54: Recipe Specific Sysroots
Resolved with PATH filtering
All required host utilities must be explicitly listed
These are all symlinked into a directory
PATH is then cleared and set to this filtered location
  HOSTTOOLS: being unavailable causes an early failure (when they can't be linked in place)
  HOSTTOOLS_NONFATAL: aren't a build failure when absent, i.e. optional tools like ccache or proxy helpers

## Slide 55: Recipe Specific Sysroots - Overview
Topics
  Definitions
  Determinism improvements in YP 2.3 +
  Future reproducibility work

## Slide 56: Recipe Specific Sysroots
Improved build system determinism
Next set our sights on the next level reproducible definition: binary reproducible builds.
Common issues that affect binary reproducibility include:
Compressing files with different levels of parallelism
Dates, times, and paths embedded in built artefacts
Timestamps of outputs changing

## Slide 57: Recipe Specific Sysroots
Future reproducibility work
Layer fetcher/Workspace setup tool – to improve ease of build environment replication
SOURCE_DATE_EPOCH – open spec to ensure consistent date/time stamps in generated artefacts
strip-nondeterminism – post-processing step to forcibly remove traces of non-determinism
etc...

## Slide 58: Activity Seven
Maintaining Your Yocto Project Based Distribution
Scott Murray

## Slide 59: Activity Nine
Kernel Modules with eSDKs
Marco Cavallini

## Slide 60: Kernel modules with eSDKs – Overview
The Extensible SDK (eSDK) is a portable and standalone development environment , basically an SDK with an added bitbake executive via devtool.
The “devtool” is a collection of tools to help development, in particular user space development.
We can use devtool to manage a new kernel module:
  Like normal applications is possible to import and create a wrapper recipe to manage the kernel module with eSDKs.

## Slide 61: Kernel modules with eSDKs – Compiling a kernel module
We have two choices
Out of the kernel tree
  When the code is in a different directory outside of the kernel source tree
Inside the kernel tree
  When the code is managed by a KConfig and a Makefile into a kernel directory

## Slide 62: Kernel modules with eSDKs – Pro and Cons of a module outside the kernel tree
When the code is outside of the kernel source tree in a different directory
Advantages
  Might be easier to handle modifications than modify it into the kernel itself
Drawbacks
  Not integrated to the kernel configuration/compilation process
  Needs to be built separately
  The driver cannot be built statically

## Slide 63: Kernel modules with eSDKs – Pro and Cons of a module inside the kernel tree
When the code is inside the same directory tree of the kernel sources
Advantages
  Well integrated into the kernel configuration and compilation process
  The driver can be built statically if needed
Drawbacks
  Bigger kernel size
  Slower boot time

## Slide 64: Kernel modules with eSDKs – The source code
#include <linux/module.h>
#include <linux/kernel.h>
static int __init hello_init(void)
{
printk("When half way through the journey of our life\n");
return 0;
}
static void __exit hello_exit(void)
{
printk("I found that I was in a gloomy wood\n");
}
module_init(hello_init);
module_exit(hello_exit);
MODULE_LICENSE("GPL");
MODULE_DESCRIPTION("Greeting module from the Divine Comedy");
MODULE_AUTHOR("Dante Alighieri");

## Slide 65: Kernel modules with eSDKs – The Makefile
obj-m += hellokernel.o SRC := $(shell pwd) all: $(MAKE) -C $(KERNEL_SRC) M=$(SRC) modules modules_install: $(MAKE) -C $(KERNEL_SRC) M=$(SRC) modules_install
KERNEL_SRC is the location of the kernel sources.
This variable is set to the value of the STAGING_KERNEL_DIR within the module class (module.bbclass)
Sources available on https://github.com/koansoftware/simplest-kernel-module.git
Notes: Note in do_install, the ‘/’ is NOT missing between ${D}${bindir}
We cd ${S} because default is ${B}, no source in ${B} (not default same as ${S} anymore)

## Slide 66: Kernel modules with eSDKs – Devtool setup
Start a new Shell! Otherwise, the existing bitbake environment can cause unexpected results
Here is how the eSDK was prepared for this class account:
This installed the eSDK into: /scratch/sdk/qemuarm
< DO NOT ENTER THE FOLLOWING COMMANDS : ALREADY EXECUTED >
$ cd /scratch/working/build-qemuarm/tmp/deploy/sdk/
$ ./poky-glibc-x86_64-core-image-base-armv5e-toolchain-ext-2.4.sh \
-d /scratch/sdk/qemuarm -y

## Slide 67: Kernel modules with eSDKs – Overview
Starting from now we are using the eSDK and not the project
During this exercise we using two different machines
  The HOST containing the eSDK (providing devtool)
  The TARGET running the final qemuarm image
Host
eSDK:~$
Target
root@qemuarm:~$

## Slide 68: Kernel modules with eSDKs – Globalsetup
Open two terminal windows and setup the eSDK environment in each one
SDK environment now set up
Additionally you may now run devtool to perform development tasks.
Run devtool --help for further details
$ source /scratch/sdk/qemuarm/environment-setup-armv5e-poky-linux-gnueabi

## Slide 69: Kernel modules with eSDKs – build the target image
Open two terminal windows and setup the eSDK environment in each one
This will create a new image into: /scratch/sdk/qemuarm/tmp/deploy/images/qemuarm
$ devtool build-image

## Slide 70: Kernel modules with eSDKs – build the target image
Run the image to check if everything is OK
This will run the Qemu machine in the TARGET shell you were using
Login using user : root (no password required)
$ runqemu qemuarm nographic

## Slide 71: Kernel modules with eSDKs – Hooking a new module into the build
Run the devtool to add a new recipe (on the HOST side)
  This generates a minimal recipe in the workspace layer
  This adds EXTERNALSRC in an workspace/appends/simplestmodule_git.bbappend file that points to the sources
  In other words, the source tree stays where it is, devtool just creates a wrapper recipe that points to it
Note: this does not add your image to the original build engineer’s image, which requires changing the platform project’s conf/local.conf
$ devtool add --version 1.0 simplestmodule \
/scratch/src/kmod/simplest-kernel-module/

## Slide 72: After the add
Workspace layer layout
$ tree /scratch/sdk/qemuarm/workspace/ /scratch/sdk/qemuarm/workspace/ ├── appends │ └── simplestmodule_git.bbappend ├── conf │ └── layer.conf ├── README └── recipes └── simplestmodule └── simplestmodule_git.bb
Notes: The build directory

## Slide 73: Kernel modules with eSDKs – Build the Module
Build the new recipe (on the HOST side)
This will create the simplestmodule.ko kernel module
This downloads the kernel sources (already downloaded for you): linux-yocto-4.12.12+gitAUTOINC+eda4d18ce4_67b62d8d7b-r0 do_fetch
$ devtool build simplemodule

## Slide 74: Kernel modules with eSDKs – Deploy the Module
Get the target’s IP address from the target serial console
root@qemuarm:~# ifconfig
In the eSDK (HOST) shell, deploy the output (the target’s ip address may change)
NOTE: the ‘-s’ option will note any ssh keygen issues, allowing you to (for example) remove/add this IP address to the known hosts table
$ devtool deploy-target -s simplestmodule root@192.168.7.2

## Slide 75: Kernel modules with eSDKs – Deploy Details
In the target (qemuarm), observe the result of deployment
devtool_deploy.list 100% 108 0.1KB/s 00:00
devtool_deploy.sh 100% 1017 1.0KB/s 00:00
./
./lib/
./lib/modules/
./lib/modules/4.12.12-yocto-standard/
./lib/modules/4.12.12-yocto-standard/extra/
./lib/modules/4.12.12-yocto-standard/extra/hellokernel.ko
./usr/
./usr/include/
./usr/include/simplestmodule/
./usr/include/simplestmodule/Module.symvers
./etc/
./etc/modprobe.d/
./etc/modules-load.d/
NOTE: Successfully deployed
/scratch/sdk/qemuarm/tmp/work/qemuarm-poky-linux-gnueabi/simplestmodule/

## Slide 76: Kernel modules with eSDKs – Load the Module
In the target (qemuarm), load the module and observe the results
root@qemuarm:~# depmod -a
root@qemuarm:~# modprobe hellokernel
[ 874.941880] hellokernel: loading out-of-tree module taints kernel.
[ 874.960165] When half way through the journey of our life
root@qemuarm:~# lsmod
Module Size Used by
hellokernel 929 0
nfsd 271348 11

## Slide 77: Kernel modules with eSDKs – Unload the Module
In the target (qemuarm), unload the module
root@qemuarm:~# modprobe -r hellokernel
[ 36.005902] I found that I was in a gloomy wood
root@qemuarm:~# lsmod
Module Size Used by
nfsd 271348 11

## Slide 78: Kernel modules with eSDKs – automatic load of the module at boot
In the target (qemuarm), edit the file below and add a new line containing the module name ‘hellokernel’
• Then reboot the Qemu machine and verify
root@qemuarm:~# vi /etc/modules-load/hello.conf
< insert the following line and save >
hellokernel
root@qemuarm:~# reboot

## Slide 79: Activity Ten
Analytics and the Event System
David Reyna

## Slide 80: Introduction
Thesis:
  The bitbake event system, together with the event database that comes with Toaster, can be used to generate and provide access to analytical data and provide a new unique toolset to solve difficult problems
What we will cover today:
  The problem space for extracting and analyzing data
  Introduce the bitbake event system, interfaces
  Event Examples: Toaster, CLI tools, customized bitbake UI
  Resources
The full presentation can be found here:
  http://events.linuxfoundation.org/sites/events/files/slides/BitbakeAnalytics_ELC_Portland.pdf
What that presentation additionally covers:
  Deep dive on the event system code and components
  Event database, database schema, custom events, custom tools, use cases, gotchas

## Slide 81: The Problem Space (as I see it)
Types of addressable problems with analytics:
  Issues with time or coincident sensitivity
  Issues with transient data values
  Issues with transient UFOs (Unidentified Failing Objects)
  Issues with trends (size, time, cache misses, scaling)
  If the problem is a needle, where is the haystack to look in
We need:
  Easy access to deep data, time, and ordering
  Reliable interaction with bitbake
  Easy access to the data with tools, both provided and custom
  Ability to acquire long term data, from a day to many months
  Keep bitbake as pristine as possible
My builds are working, do I need this?
  Excellent, you are in good shape! However, if they stop working or when you do new work or try to scale, here are additional tools for your toolbox

## Slide 82: The Problem Space (2)
Well known and documented data from bitbake builds:
  Logs (Build/Error logs)
  Artifacts (Kernel, Images, SDKs)
  Manifests (Image content, Licenses)
  Variables (bitbake -e)
  Dependencies
However…
  These only capture the final results of the build, not how the build progressed nor the intermediate or analytical information.
  It is hard for example to correlate logs with other logs, let alone with other builds
The Answer!
  The bitbake event system
  The bitbake event database
  Events are easy to create, fire, listen to, and catch
  There are more than 40 existing event types
  Uses IPC over python xmlrpc sockets, with automatic data marshalling

## Slide 83: Toaster Analytics – Intermediate Data Example
The Toaster database/GUI can for example display the intermediate values of bitbake variables, specifically each variable’s modification history down to the file and line.

## Slide 84: Overview of Available Events
BuildInit|BuildCompleted|BuildStarted
ConfigParsed|RecipeParsed
ParseCompleted|ParseProgress|ParseStarted
MultipleProviders|NoProvider
runQueueTaskCompleted|runQueueTaskFailed|runQueueTaskSkipped| runQueueTaskStarted
TaskBase|TaskFailed|TaskFailedSilent|TaskStarted| TaskSucceeded
sceneQueueTaskCompleted|sceneQueueTaskFailed|sceneQueueTaskStarted
CacheLoadCompleted|CacheLoadProgress|CacheLoadStarted
TreeDataPreparationStarted|TreeDataPreparationCompleted
DepTreeGenerated|SanityCheck|SanityCheckPassed
MetadataEvent
LogExecTTY|LogRecord
CommandCompleted|CommandExit|CommandFailed
CookerExit

## Slide 85: Event Clients (you are already an event user!)
Bitbake actually runs in a separate context, and expects an event client (called a “UI") to display bitbake's status and output
Here are the existing bitbake event clients:
  Knotty: this is the default bitbake command line user interface that you know and love. It uses events to display the famous dynamic task list, and to show the various progress bars
  Toaster: this is the bitbake GUI, which provides both a full event database and a full feature web interface. We will be using this as our primary example since it contains the most extensive implementation and support for events
  Depexp: this executes a bitbake command to extract dependency data events, and then uses a GTK user interface to interact with it
  Ncurses: this provides a simple ncurses-based terminal UI

## Slide 86: Event Database
The event database is built into Toaster to maintain persistent build data
It can however just as easily be used directly with command line scripts or other SQL compatible tools
Bitbake
Event Database (SQL)
Toaster GUI Server
Toaster Event Client
User Web Client
Knotty Event Client
User Console
User Console
Python Script

## Slide 87: Example Event Database with CI Builders
If you enable the Toaster UI in a CI system, you can additionally get the event artifacts together with your build artifacts (you will definitely need to select a production level database)
Bitbake
Event Database (SQL)
Toaster Event Client
Knotty Event Client
Continuous Integration Build System
Lost event data

## Slide 88: Adding Build Data to the Event Database
There are two easy ways to get build data into the event database
  Create and execute your builds from within the Toaster GUI
  Start Toaster, and run your command line builds in that environment
The ‘source toaster’ performs these tasks
  Creates the event database if not present, applies any schema updates
  Starts the web client (this can be ignored for command line usage)
  Sets the command line environment to use Toaster as the UI for bitbake (“BITBAKE_UI”)
$ cd /scratch
$ source poky/oe-init-build-env
$ source toaster start webport=0.0.0.0:8000 # local only: “127.0.0.1:8000”
$ firefox localhost:8000 # here, connect browser from your using Toaster URL
$ . Poky/oe-init-build-env
$ source toaster start webport=0.0.0.0:8000
$ bitbake <whatever>

## Slide 89: Example 1: Custom command line analytic tool

## Slide 90: Minimal Event Database Python Script
Accessing the data in the event database is very simple. In this example we will print the data from the first-most Build record, and also look up and print the associated Target record
$ cat sample_toaster_db_read.py
#!/usr/bin/env python3
import sqlite3
conn = sqlite3.connect('toaster.sqlite')
c = conn.cursor()
c.execute("SELECT * FROM orm_build")
build=c.fetchone()
print('Build=%s' % str(build))
c.execute("SELECT * FROM orm_target where build_id = '%s'" % build[0])
print('Target=%s' % str(c.fetchone()))
$
$ ./sample_toaster_db_read.py
Build=(1, 'qemux86-64', 'poky', '2.2.1', '2017-02-12 23:55:52.137355', \
'2017-02-13 00:16:30.794711', 0, '/…/build_20170212_235552.805.log', \
'1.32.0', 1, 1478, 1478, '20170212235604')
Target=(1, 'core-image-base', '', 1, 0, ‘/…/license.manifest', 1, \
'/…/core-image-base-qemux86-64-20170212235604.rootfs.manifest')$

## Slide 91: Full Feature Event Database Python Script
In this section we will work with an example python application that extracts and analyzes event data
Specifically, we will attempt to investigate the question: “How exactly do the tasks of a build overlap execution with other tasks, and on a higher level how to recipes overlap execution with other recipes, plus what data can extract around this question”
While this may not be a deep problem, and there are certainly OE tools that already provide similar information (e.g. pybootchart), the point is that (a) this was very easy and fast to write, and (b) you can now fully customize the analysis and output to your needs and desires.

## Slide 92: Task and Recipe Build Analysis Script
Here is the list of available commands and features
$ more event_overlap.py # see db setup and schema info
$ ./event_overlap.py --help
Commands: ?
? : show help
b,build [build_id] : show or select builds
d,data : show histogram data
t,task [task] : show task database
r,recipe [recipe] : show recipes database
e,events [task] : show task time events
E,Events [recipe] : show recipe time events
o,overlap [task|0|n] : show task|zero|n_max execution overlaps
O,Overlap [recipe|0|n] : show recipe|zero|n_max execution overlaps
g,graph [task] [> file] : graph task execution overlap
G,Graph [recipe] [> file] : graph recipe execution overlap
h,html [task] [> file] : HTML graph task execution overlap [to file]
H,Html [recipe] [> file] : HTML graph recipe execution overlap [to file]
q,quit : quit
Examples:
* Recipe/task filters accept wild cards, like 'native-*, '*-lib*'
* Recipe/task filters get an automatic wild card at the end
* Task names are in the form 'recipe:task', so 'acl*patch'
will specifically match the 'acl*:do_patch' task
* Use 'o 2' for the tasks in the two highest overlap count sets
* Use 'O 0' for the recipes with zero overlaps

## Slide 93: Histogram of Parallel Task/Recipe Execution (‘d’)
Commands: d
Histogram:For each task, max number of tasks executing in parallel
0 1 2 3 4 5 6 7 8 9
----------------------------------------
0) 0 621 16 22 50 49 56 83 94 45
10) 57 82 87 81 47 56 58 62 64 88
20) 121 182 268 221 148
Histogram:For each recipe's task set, max number of recipes executing in parallel
0 1 2 3 4 5 6 7 8 9
----------------------------------------
0) 0 5 1 1 1 1 1 1 3 3
10) 1 2 2 2 2 1 1 3 1 6
20) 1 1 2 1 1 2 2 1 1 1
30) 1 1 2 2 1 3 1 2 2 1
40) 1 1 1 1 1 1 1 1 3 1
50) 1 2 4 2 2 1 1 1 1 2
60) 1 2 1 1 1 2 1 1 1 2
70) 1 1 2 2 2 2 1 3 3 1
80) 3 2 1 1 1 10 7 8 8 8
90) 7 7 2 2 3 2 2 1 1 2
100) 2 1 1 1 2 2 1 3 2 3
110) 2 1 2 1 1 1 1 2 1 1
120) 2 1 1 2 1 1 1 2 1 2
130) 1 1 1 1

## Slide 94: Histogram of Overlapping Task/Recipe Execution
…
Histogram:For each task, max number of tasks that overlap its build
0 1 2 3 4 5 6 7 8 9
----------------------------------------
0) 614 9 10 29 28 42 46 55 51 47
10) 56 52 48 59 28 33 63 29 43 60
20) 60 94 119 223 105 95 53 57 36 40
30) 20 26 15 17 13 8 11 9 9 2
40) 7 10 9 7 3 6 6 3 6 6
50) 6 6 6 2 2 5 3 1 3 1
60) 4 2 5 1 2 2 1 2 3 5
... (sparse) ...
980) 0 0 1
Histogram:For each recipe's task set, max number of recipes that overlap its build
0 1 2 3 4 5 6 7 8 9
----------------------------------------
0) 67 0 0 0 0 0 0 0 0 0
10) 0 0 0 0 0 0 0 0 0 0
... (all zeros) ...
80) 0 0 0 0 5 1 1 8 4 1
90) 3 2 0 1 4 4 3 0 0 0
100) 0 0 0 0 0 0 2 1 0 0
110) 2 0 1 2 0 0 3 0 1 2
120) 0 0 0 0 0 0 0 0 2 0
130) 0 26 8 5 2 6 5 0 0 1
... (sparse) ...
170) 0 4 0 0 0 0 0 0 0 0
180) 0 0 0 0 0 0 69

## Slide 95: Initial Results
Here are some initial results when examining a “core-image-minimal” project with Task Count=2658 and Recipe Count=254
We have as many as 148 tasks being able to run with all 24 available threads used
There were 621 tasks that ran solo
There were zero recipes that ran solo
There was one task “linux-yocto:do_fetch” whose execution overlapped with 983 other tasks; the second most overlap was “python3-native:do_configure” with an overlap count of 798
There were 69 recipes that overlaps with 186 other recipes, with the next highest overlap being 4 recipes that overlap with 171 other recipes
The below sample HTML output page on task overlaps shows the amount of information available, with the recipe page too large to show in this context

## Slide 96: Initial Results
Let us see the available builds:
Select the minimal build #4
Run the commands d,t,r,o,O,g,G to get a sense of the minimal outputs
Command: b
List of available builds:
BuildId=1) CompletedOn=2017-02-13 00:16:30.794711, Outcome=SUCCEEDED,
Project=Command line builds, Target=core-image-base, Task=''
BuildId=2) CompletedOn=2017-02-13 00:46:40.724932, Outcome=FAILED,
Project=Command line builds, Target=core-image-base, Task=populate_sdk_ext
BuildId=3) CompletedOn=2017-02-13 00:46:26.513568, Outcome=SUCCEEDED,
Project=Command line builds, Target=core-image-base, Task=''
BuildId=4) CompletedOn=2017-02-23 09:02:31.109727, Outcome=SUCCEEDED,
Project=Command line builds, Target=quilt-native, Task=''
Command: b 4
Fetching build #4
Build: CompletedOn=2017-02-23 09:02:31.109727, Outcome=SUCCEEDED,
Project='Command line builds‘ Target='quilt-native', Task='', Machine='qemux86-64'
Success: build #4, Task Count=9, Recipe Count=1

## Slide 97: Initial Results
Now select the large build (#1) and explore. We shall use the recipe filter ‘zlib’ to limit the output:
Make sure your window is very wide, and then run this command to see a graph of the task overlaps for zlib:
Command: b 1
Command: o zlib
Command: e zlib
Command: t zlib
Command: r zlib
Command: o zlib
Command: O 0
Command: g zlib

## Slide 98: Sample HTML Output of Task Overlap

## Slide 99: Example 2: Custom Event Interface (knice)

## Slide 100: Custom Event UI
If the knotty UI is too simple (since it does not collect data) and the Toaster UI too large for your analytic needs, you can make your own bitbake UI and have it handle specific events as you need. Here is a simple tutorial on how to do that.
What we will do is start with the “knotty” UI, and then customize it as the “knice” UI.
We make a simple change:
Now we run it:
$ pushd ../bitbake/lib/bb/ui
$ cp knotty.py knice.py
$ sed –i –e "s/notty/nice/g" knice.py
$ vi knice.py
-print("Nothing to do. Use 'bitbake world' to build everything, \
or run 'bitbake --help' for usage information.")
+print(“NICE: Nothing to do. Use 'bitbake world' to build everything, \
or run 'bitbake --help' for usage information.")
$ popd
$ bitbake -u knice
NICE: Nothing to do. Use 'bitbake world' to build everything, or run
'bitbake --help' for usage information.

## Slide 101: Custom Event UI (2)
Now let us instrument an event by updating “knice.py”.
First, let us add "bb.event.DepTreeGenerated“ to the event list
Now let us add a print statement to the otherwise empty "bb.event.DepTreeGenerated“ handler code
Now we run it and see our code run!
$ vi ../bitbake/lib/bb/ui/knice.py
- "bb.event.ProcessFinished"]
+ "bb.event.ProcessFinished","bb.event.DepTreeGenerated"]
if isinstance(event, bb.event.DepTreeGenerated):
+ logger.info("NICE: bb.event.DepTreeGenerated received!")
continue
[build]$ bitbake -u knice quilt-native [ | grep NICE ]
...
NOTE: NICE: bb.event.DepTreeGenerated received! | ETA: 0:00:00
...

## Slide 102: Resources
Source code and example event database
  This is available as part of the Yocto Project Developer Day Advanced Class (see https://www.yoctoproject.org/yocto-project-dev-day-north-america-2017, and https://wiki.yoctoproject.org/wiki/DevDay_US_2017 )
Here is the Toaster documentation, and Youtube video!
  http://www.yoctoproject.org/docs/latest/toaster-manual/toaster-manual.html#toaster-manual-start
  https://youtu.be/BlXdOYLgPxA
Basic information about bitbake UI’s
  http://elinux.org/Bitbake_Cheat_Sheet
Here is design information on the event model for Toaster
  https://wiki.yoctoproject.org/wiki/Event_information_model_for_Toaster
Here is the original design information on Toaster and bitbake communication
  https://wiki.yoctoproject.org/wiki/Toaster_and_bitbake_communications

## Slide 103: Bonus Example 3: Custom event types

## Slide 104: Custom events
Normally, for a custom event you merely sub-class the event class or some other existing class, and add your new content
In this example, we show how we can easily extend "MetadataEvent" and use it on the fly, since the sub-event 'type' is an arbitrary string and the data load is a simple dictionary.
Event creation:
Event handler:
my_event_data = {
"TOOLCHAIN_OUTPUTNAME": d.getVar("TOOLCHAIN_OUTPUTNAME")
}
bb.event.fire(bb.event.MetadataEvent("MyMetaEvent", my_event_data), d)
if isinstance(event, bb.event.MetadataEvent):
if event.type == "MyMetaEvent":
my_toochain = event.data["TOOLCHAIN_OUTPUTNAME"]

## Slide 105: Bonus Example 4: Debugging coincident data in bitbake

## Slide 106: Using Events for debugging bitbake
You can also use the event system in debugging bitbake or your classes.
Example 1: The quintessential example is to use “logger.info()” to insert print statements into the code. This is implemented as an event, meaning that will it be passed to the correct external UI and not lost in some random log file.
Example 2: The ESDK file used to be copied to the build’s “deploy/sdk” directory as part of the task “populate_sdk_ext”. However, it is somehow happening later, and it is hard reading the code to determine when and where that is now occurring. We can use the event stream to help narrow down the candidates.
  First, we add a log call into the event read loop in “bitbake/lib/bb/ui/toasterui.py”. This will provide a log of the received events as they go by, and also reveal when the ESDK file is created.
I then run a build (in the Toaster context):
logger.info(“FOO:"+str(event)+","+
str(os.path.isfile('<path_to_esdk_file>')) )

## Slide 107: Using Events for debugging bitbake (2)
  Second, we then run a build (in the Toaster context) and collect the events:
  Third, we examine the log to find when the file’s state changed.
  We see that the existing ESDK file was removed after “bb.event.DepTreeGenerated”, and placed after “sstate-build-populate_sdk_ext”. In other words it was moved out of the main “populate_sdk_ext” task and into its sstate task. QED.
$ bitbake do_populate_sdk_ext > my_eventlog.txt
...
NOTE: FOO:<bb.event.DepTreeGenerated object at 0x7f94ec829710>,True
NOTE: FOO:<bb.event.MetadataEvent object at 0x7f94ec829358>,False
...
NOTE: FOO:<LogRecord: ... "Executing buildhistory_get_extra_sdkinfo ...">,False
...
NOTE: FOO:<LogRecord: BitBake.Main, ... sstate-build-populate_sdk_ext ...">,False
NOTE: FOO:<bb.build.TaskSucceeded object at 0x7f94e7f5f358>,True
…

## Slide 108: Bonus Example 5: Toaster

## Slide 109: Adding Build Data to the Event Database
There are many existing analytic views in Toaster
Start the Toaster GUI in the build directory (with open ports)
On your host, open your browser to: http://devday-a.yocto.io:30000(+your session number)
Click on “All Builds”, and select a build
Click on “Time”, “CPU Usage”, and “Disk I/O”
Click on “Tasks”, and see the task order and cache usage
$ source toaster start webport=0.0.0.0:8000

## Slide 110: Existing Toaster Analytics
The Toaster GUI already provides analytical data on builds, for example on sstate cache success rate, task execution time, CPU usage, and Disk I/O

## Slide 111: Activity Nine
Kernel And Security Open Forum
Staff

## Slide 112: Open Topics
Kernel:
  Is the YP-2.2 kernel already obsolete?
  Kernel fragments for any kernel without explicit inherit?
  Enhanced kernel audit details?
  Distro and kernel feature integration?
Security
  The Yocto Project has a general policy for sustaining (released) branches. We tend to fix individual security issues (CVE) instead of upgrade.
  There is a Yocto Project security mailing list: yocto-security@yoctoproject.org
  Low volume. We are working on automatically mailing patches that include the CVE tag to the mailing list so it is searchable, but we have not yet done so.

## Slide 113: Open Topics
This is tracked by including the relevant CVE tag, pointing to the CVE information in the patches themselves, such as:
The above version includes a fix, documents it (CVE: CVE-2016-6321), and then also documents where the fix came from (upstream commit 7340f67 of that project).
+From 7340f67b9860ea0531c1450e5aa261c50f67165d Mon Sep 17 00:00:00 2001
+From: Paul Eggert <eggert@Penguin.CS.UCLA.EDU>
+Date: Sat, 29 Oct 2016 21:04:40 -0700
+Subject: [PATCH] When extracting, skip ".." members
+
+* NEWS: Document this.
+* src/extract.c (extract_archive): Skip members whose names contain
+"..".
+
+CVE: CVE-2016-6321
+Upstream-Status: Backport
+
+Cherry picked from commit: 7340f67 When extracting, skip ".." members
+
+Signed-off-by: Sona Sarmadi <sona.sarmadi@enea.com>

## Slide 114: Questions and Answers

## Slide 115: Thank you for your participation!

## Slide 116: Appendix: Board Bring-up

## Slide 117: MinnowBoard Max Turbot SD Card Prep
Here is how to flash the microSD card for the MBM
Insert the microSD card into your reader, and attach that to your host
  Find the device number for the card (e.g. “/dev/sdc”). For example run “dmesg | tail” to find the last attached device
  Unmount any existing partitions from the SD card (for example “umount /media/<user>/boot”)
  Flash the image $ sudo dd if=tmp/deploy/images/intel-corei7-64/core-image-base-intel-corei7-64.hddimg of=<device_id> bs=1M
  On the host, right-click and eject the microSD card’s filesystem so that the image is clean

## Slide 118: MinnowBoard Max Turbot SD Card Prep
Note: you can instead use the automatically generated WIC image
  Flash the image $ sudo dd if=scratch/working/build-mbm/tmp/deploy/images/intel-corei7-64/core-image-base-intel-corei7-64.wic of=<device_id> bs=1M
  Note that when the target boots, the WIC version of the image the kernel boot output does not appear on the serial console. This means that after 14 seconds of a blank screen you will then see the login prompt

## Slide 119: MinnowBoard Max Turbot Board Bring-up
Setting up the board connections
  Unpack the target
  Insert the provided micro-SD card (pin side up)
  Attach the ethernet cable from the target to the hub
  Attach the FTDI 6-pin connector. The BLACK wire is on pin 1, which has an arrow on the silk-mask and is on the center-side of the 6-pin inline connector near the microSD connector
  Connect the FTDI USB connector to your host (Note: the USB serial connection will appear on your host as soon as the FTDI cable is connected, regardless if the target is powered)
Start your host’s console for the USB serial console connection
  On Linux, you can use the screen command, using your host’s added serial device (for example “/dev/ttyUSB0):
      $ screen /dev/ttyUSB0 115200,cs8 (FYI: “CTRL-A k” to kill/quit)
  On Windows, you can use an application like “Teraterm”, set the serial connection to the latest port (e.g. “COM23”), and set the baud rate to 115200 (“Setup > Serial Port… > Baud Rate…”)

## Slide 120: MinnowBoard Max Turbot Board Bring-up (2)
Start the board
  Connect the +5 Volt power supply to the target
  You should see the board’s EFI boot information appear in your host’s serial console
Run these commands to boot the kernel Shell> connect -r Shell> map -r Shell> fs0: Shell> bootx64
You should now see the kernel boot
At the login prompt, enter “root”
Note: see the appendix on instructions on how we create the microSD card images

## Slide 121: Dragon Board SD Card Prep
TBD

## Slide 122: Beagle Bone SD Card Prep
TBD

## Slide 123: Bonus Activity
Node.js
Henry Bruce

## Slide 124: Introduction
Additional Project Setup
  tbd
Credits: Brendan Le Foll and Paul Eggleton
Notes: We're here to learn about devtool's recently added support for Node.js
This is not a Node.js masterclass, but some knowledge of npm and JavaScript will be helpful.
I am not a Node.js expert, but am a proponent of this work due to its growing popularity in the IoT space
A shout out to Brendan Le Foll who started Node.js support and Paul Eggleton who has greatly enhanced it.

## Slide 125: What we’ll be doing
Understanding Node.js support in Open Embedded
Using devtool to auto-generate Node.js recipes
Building and deploying a package
On-target Node.js application development
Using devtool to package the application
Discuss known issues and plans for future work

## Slide 126: Node.js and Open Embedded
Layer index recipe search returns ~10 hits
  We’ll be working with the meta-oe recipe
  (4.x, oldest LTS version)
More versions are available in meta-nodejs
Devtool support was introduced in krogoth
  Use pyro
There’s still work to do. See bug #10653.

## Slide 127: Using devtool to generate recipe
Go to the build directory (with a clean shell) $ cd /scratch $ . poky/oe-init-build-env
Create recipe from module in registry
  $ devtool add "npm://registry.npmjs.org;name=mraa;version=1.5.1“ -- or --
  b) $ devtool add /scratch/src/nodejs/mraa-1.5.1.tgz
Parses package.json for basis of recipe
  Package name and version
  Description, homepage
  Location of source
  Licenses
Recursively goes through dependencies
  Creates shrinkwrap and lockdown files
$ devtool edit-recipe mraa

## Slide 128: Under the hood
NPM makes it hard to limit network access to fetch task
Fetch task walks dependency tree fetching tarballs from NPM registry
Build task uses ‘npm install’ with registry disabled (OE specific patch) to create node_modules
Install tasks puts node_modules in correct place

## Slide 129: Building and deploying
Build is really a pre-package task (apart from native gyp builds)
$ devtool build mraa
Deploy as normal
$ devtool deploy-target -s mraa root@target_addr
Is module installed on the target?
# npm -g ls mraa
Notes: Note that package version does not match module version. Ideally it should

## Slide 130: Running on target
# export NODE_PATH=/usr/lib/node_modules
# node
> var mraa = require(‘mraa’)
> console.log(‘mraa board: ‘ + mraa.getPlatformName())
> var gpio = new mraa.Gpio(360, true, true)
> gpio.dir(mraa.DIR_OUT)
> gpio.write(1)

## Slide 131: Developing on target
Many ways of doing this. Let’s keep it simple
On your target
# mkdir mmax-blinker
# cd mmax-blinker
Write some code and test it
  # cp $NODE_PATH/mraa/examples/javascript/Blink-IO.js .
  # vi Blink-IO.js
            change GPIO to “raw” id 360
            add #!/usr/bin/node
  # node Blink-IO.js

## Slide 132: Create NPM module on target
Create package.json
  # cp $NODE_PATH/mraa/COPYING .
  # npm init
  # vi package.json
          Add “bin” entry. Local dependency for mraa (or skip)
Install
  # npm -g install
Test
  # mmax-blinker

## Slide 133: Create package for your application
Copy files to build host
  scp –r root@x.x.x.x:mmax-blinker mmax-blinker
Check dependencies
  Local dependencies are for development only
Now create package
  $ devtool add /path/to/mmax-blinker
  $ devtool edit-recipe mmax-blinker

## Slide 134: Build, deploy and run application
Build
  $ devtool build mmax-blinker
Deploy
  $ devtool deploy-target mmax-blinker root@x.x.x.x
  # ln -s /usr/lib/node_modules/mmax-blinker/Blink-IO.js /usr/bin/mmax-blinker
  # chmod +x /usr/bin/mmax-blinker
Run
  # mmax-blinker

## Slide 135: Keep in Touch
https://wiki.yoctoproject.org/wiki/Nodejs_Workflow_Improvements