## Slide 1: Developer Day Class
Stephano Cetola, Armin Kuster, Scott Murray, David Reyna,
Rudolf J Streif, Joshua Watt
Yocto Project Developer Day  San Diego  20 August 2019

## Slide 2: Advanced Class
Class Content (download these slides!):
  https://wiki.yoctoproject.org/wiki/DevDay_San_Diego_2019
  Lab Requirements:
            Wireless connection: same as ELCE conference
            SSH (Windows: e.g. “putty”)
Wireless Registration:
  Will be passed out

## Slide 3: Agenda – The Developer Day Class
9:00- 9:10 Keynote
9:10- 9:15 Lab account setup
9:15-10:15 Hash Equivalency/Runqueue
10:15-10:30 Morning Break
10:30-12:00 User Space Topics
12:00-12:30 Lunch
12:30- 1:10 Package Feeds
1:10- 1:40 Mirrors and SState
1:40- 2:40 WIC
2:10- 2:30 Afternoon Break
2:30- 3:30 Container building/Multiconfig
3:30- 4:30 Devtool
4:30- 5:00 Tools, Toaster, User Experience
5:00- 5:30 Forum, Q and A

## Slide 4: Class Account Setup

## Slide 5: Yocto Project Dev Day Lab Setup
The virtual host’s resources can be found here:
  Your Project: "/scratch/poky/build-qemuarm“
  Extensible-SDK Install: "/scratch/sdk/qemuarm“
  Sources: "/scratch/src“
  Poky: "/scratch/poky"
  Downloads: "/scratch/downloads"
  Sstate-cache: "/scratch/sstate-cache“
You will be using SSH to communicate with your virtual server.

## Slide 6: FYI: How class project was prepared (1/2)
$
$ cd /scratch
$ git clone -b warrior git://git.yoctoproject.org/poky.git
$ cd poky
$
$ bash # set up local shell
$ # Prepare the project
$ ./scratch/poky/oe-init-build-env build
$ echo "MACHINE = \"qemuarm\"" >> conf/local.conf
$ echo "SSTATE_DIR = \"/scratch/sstate-cache\"" >> conf/local.conf
$ echo "DL_DIR = \"/scratch/downloads\"" >> conf/local.conf
$ echo "IMAGE_INSTALL_append = \" gdbserver openssh libstdc++ \
curl \"" >> conf/local.conf
$ $ # Build the project
$ bitbake core-image-base
$
Notes: ilab01@devday010:/scratch/poky/build-qemuarm$ du -sh tmp/
34G tmp/
ilab01@devday010:/scratch/poky/build-qemuarm$
$ time bitbake core-image-base
real 1m3.721s
user 0m1.805s
sys 0m0.227s
ilab01@devday010:/scratch/poky/build-qemuarm$ du -sh tmp/
2.0G tmp/

## Slide 7: FYI: How class project was prepared (2/2)
$ # Build the eSDK
$
$ bitbake core-image-base -c populate_sdk_ext
$ cd /scratch/poky/build/tmp/deploy/sdk/
$ ./poky-glibc-x86_64-core-image-base-armv5e-toolchain-ext-*.sh \
-y -d /scratch/sdk/qemuarm
$ exit # return to clean shell
$
$
$ bash # set up local shell
$ cd /scratch/sdk/qemuarm
$ . /scratch/sdk/qemuarm/environment-setup-armv5e-poky-linux-gnueabi
$ devtool modify virtual/kernel
$ exit # return to clean shell
$
Notes: ilab01@devday010:/scratch/poky/build-qemuarm$ du -sh tmp/
34G tmp/
ilab01@devday010:/scratch/poky/build-qemuarm$
$ time bitbake core-image-base
real 1m3.721s
user 0m1.805s
sys 0m0.227s
ilab01@devday010:/scratch/poky/build-qemuarm$ du -sh tmp/
2.0G tmp/

## Slide 8: NOTE: Clean Shells!
We are going to do a lot of different exercises in different build projects, each with their own environments.
To keep things sane, you should have a new clean shell for each exercise.
There are two simple ways to do it:
  Close your existing SSH connection and open a new one -- or –
  Do a “bash” before each exercise to get a new sub-shell, and “exit” at the end to remove it, in order to return to a pristine state.

## Slide 9: Activity One
Keynote
Nicolas Dechesne

## Slide 10: Outline
Project updates
Yocto Project Dev Day
Yocto Project Summit 2019
Join us!

## Slide 11: Yocto Project releases
2.6.1, 2.6.2, 2.6.3
  ~600 changes
  94 developers
2.7 and 2.7.1
  ~1900 changes
  177 developers
So far, for 3.0
  ~1500 changes
  136 developers

## Slide 12: What’s coming in 3.0 , aka “zeus”
Autobuilder infrastructure hardware refreshed
Many recipe updates, including significant removal of old or obsolete software to ensure modern and up-to-date core Linux software stack
Support for the latest host distributions
Pre-merge testing on IA and ARM using QEMU/KVM (ptest, LTP, tracking build performance)
Automated tooling to support automated recipe upgrades
Build change equivalence is detected and used to avoid rebuilding unchanged components
No other cross compiling build system is as complete or functional. Nobody has ever tried optimizations from scratch builds like the Yocto Project does.

## Slide 13: Live Coding with Yocto Project
Monthly live tutorial on Twitch, run and managed by Josef Holzmayr
https://www.twitch.tv/yocto_project/
All videos available on our Youtube channel as well: https://www.youtube.com/user/TheYoctoProject

## Slide 14: Yocto Project Dev Day
Very important event for us
  we really enjoy meeting new users
  we really value feedback from the field!
Don’t hesitate to ask questions, take as much as possible from the great speakers today!
We need more users, contributors and maintainers!
Send us feedback!

## Slide 15: Yocto Project Summit 2019
First ever Yocto Project Summit 2019
Co-located with Embedded Linux Conference Europe, Lyon, France
Oct 31st and Nov 1st 2019
Evening reception with drinks and appetizers.
CFP is open until Sept 16th
https://wiki.yoctoproject.org/wiki/index.php?title=Yocto_Project_Summit_2019

## Slide 16: Join our community
Use, participate, contribute! https://www.yoctoproject.org/community/
Public technical and engineering meetings
Spread the work at conferences and events about the cool things you build with Yocto Project
Social media:
  Stack overflow
  Twitter
  LinkedIn

## Slide 17: Activity Two
Hash Equivalency/Runqueue
Joshua Watt

## Slide 18: Outline
What is the Runqueue?
Traditional Runqueue Execution
What is the purpose of Hash Equivalence?
Runqueue Execution with Hash Equivalence Server
Signature Generation with Hash Equivalence Server
Live Demo
The Role of Reproducible Builds
Alternate Output Hash Methods
Notes: I don’t have 45 minutes of material. If you sit there listening to me drone one over my slides this will be short
Please feel free to stop me and ask questions at any time.

## Slide 19: What is the Runqueue?
Notes: How many know what the runqueue is?

## Slide 20: What is the Runqueue?
The “queue” (tree) of tasks that bitbake will execute for a given build
  Records task dependencies
  Record task state (completed, ready to run, not ready)
  As tasks are executed bitbake marks them as complete
Notes: The runqueue is the subset of all parsed recipe tasks that bitbake will execute during a build
  It is a fairly complex data structure that incorporates several lists and tree-like structures
  Tracks task states
    Completed
    Ready to Run
    Not Ready
  Tracks task dependencies and reverse task dependencies
When bitbake is ready to execute a new task, it finds one from the runqueue that is ready to run
  All dependencies are satisfied
Executes the task
When execution is complete:
  Captures the result
  Marks the task as completed
  Updates dependent tasks to check if any might now be ready to run

## Slide 21: Traditional Runqueue Execution
Notes: In order to describe how hash equivalence works, it is helpful to understand how the traditional runqueue works
Give a brief overview of the basic operation of the traditional runqueue
Greatly simplified
Many tasks are omitted for brevity

## Slide 22: Traditional Runqueue Execution
A:do_configure
taskhash: 111
A:do_populate_sysroot
taskhash: 222
B:do_configure
taskhash: 333
B:do_populate_sysroot
taskhash: 444
Notes: Two recipes are present, “A” and “B”
  Each has 2 tasks, “do_configure” and “do_populate_sysroot”
  The blue lines show dependencies
    do_populate_sysroot for each recipe depends on do_configure for that recipe
    do_configure in recipe B depends on do_populate_sysroot in recipe A
Every task has a “taskhash” that bitbake calculates at signature generation time
  Determine if a task needs to be rebuilt. Includes:
    Bitbake variables
    Task code
    Input files (e.g. SRC_URI)
    The taskhash value from dependent tasks (e.g. the taskhash for A:do_populate_sysroot includes the value “111” b/c that is the taskhash for A:do_configure)

## Slide 23: Traditional Runqueue Execution
A:do_configure
taskhash: 111
A:do_populate_sysroot:222
B:do_populate_sysroot:444
A:do_populate_sysroot
taskhash: 222
B:do_configure
taskhash: 333
B:do_populate_sysroot
taskhash: 444
Notes: Certain tasks in the runqueue are “setscene” tasks. In our example, do_populate_sysroot is an setscene task
Setscene is a property of the task itself, not the specific task instance (e.g. all do_populate_sysroot tasks are setscene tasks)
  After they execute, their output is captured into a sstate tarball and cached
    Shown in green
    This tarball can be shared between multiple hosts
  Note that the sstate cache objects are named based on the taskhash of the task that created them
    Any particular sstate tarball is only intended to replace a task with the same task hash

## Slide 24: Traditional Runqueue Execution
A:do_populate_sysroot:222
A:do_populate_sysroot_setscene
taskhash: 222
B:do_configure
taskhash: 333
B:do_populate_sysroot
taskhash: 444
Notes: If bitbake sees a setscene task that it has not executed before has a sstate object, it will execute the “setscene” task in place of the actual task and skip all it’s dependencies
  In our example, do_populate_sysroot from recipe A can be replaced by do_populate_sysroot_setscene which is restored from the previous sstate object
    This skips executing do_configure for recipe A and all other upstream dependent tasks
In the traditional runqueue, all setsecene tasks are run in a sperate phase of the build before the normal tasks
  Bitbake can’t “go back” and run more setscene tasks after it has started normal task execution

## Slide 25: Traditional Runqueue Execution
A:do_configure
taskhash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
A:do_populate_sysroot
taskhash: bbb
B:do_configure
taskhash: ccc
B:do_populate_sysroot
taskhash: ddd
Notes: What happens when a task’s taskhash changes (e.g. do_configure in recipe A)?
  This will change all downstream taskhashes
    b/c each task uses the value from the dependent taskhash
  Renders the previously cached sstate objects unused
    Sometimes, this is what you want
      Significant changes in function
      Changes to what a recipe provides for others to use
    Sometimes those sstate objects would still be valid because the taskhash change wouldn’t change their contents
      In these cases rebuilding is actually unnecessary
Questions on how the traditional runqueue works before moving on?

## Slide 26: What is the purpose of Hash Equivalence?
Improve the reuse of sstate
Reduce unnecessary rebuilds of recipes
Reduce build times
Notes: The goal of hash equivalence is to improve the situation just described where a trivial change to the do_configure task left the sstate object unused.
Thus, hash equivalence should
Improve the resuse of sstate in the face of trivial changes
Which will reduce unnecessary rebuilds of recipes
Which will reduce build times
Which will make everyone happy

## Slide 27: Runqueue Execution with Hash Equivalence Server
Notes: Let’s take a look at what the modern runqueue looks like with the hash equivalence server

## Slide 28: Runqueue Execution with Hash Equivalence Server
A:do_configure
taskhash: 111
unihash: 111
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
A:do_populate_sysroot
taskhash: 222
unihash: 222
B:do_configure
taskhash: 333
unihash: 333
B:do_populate_sysroot
taskhash: 444
unihash: 444
Notes: A new hash is introduced for all tasks called the “unique hash” abbreviated “unihash”
  Unless told otherwise, bitbake assumes the unihash is the same as the taskhash
  The rules for calculating a task’s taskhash are modified so that it includes the value of the unihash for dependent tasks instead of taskhash
  sstate tarballs are named based on unihash instead of taskhash
  Note: This results in no change to the semantics of the runqueue unless there is outside influence on the unihashes

## Slide 29: Runqueue Execution with Hash Equivalence Server
A:do_configure
taskhash: 111
unihash: 111
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
A:do_populate_sysroot
taskhash: 222
unihash: 222
outhash: 123
B:do_configure
taskhash: 333
unihash: 333
B:do_populate_sysroot
taskhash: 444
unihash: 444
Notes: When a hash server is enabled, and additional step takes place for setscene enabled tasks
  After the task runs
  Before sstate tarball is created
  An “output hash” a.k.a. “outhash” is calculated for the task output
    The current implementation checksums all the files and metadata that will go into the sstate tarball
      other methods can be implemented
  The output hash and taskhash are reported to the server, which stores them in a persistent database

## Slide 30: Runqueue Execution with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
A:do_populate_sysroot
taskhash: bbb
unihash: bbb
B:do_configure
taskhash: ccc
unihash: ccc
B:do_populate_sysroot
taskhash: ddd
unihash: ddd
Notes: Change A:do_configure’s taskhash again
  Assume this is a trivial change that doesn’t actually change the task output
As before, the taskhashes change in all downstream tasks
  Unihashes also change
  sstate objects cannot be used
  No setscene tasks are executed

## Slide 31: Runqueue Execution with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot
taskhash: bbb
unihash: 222
outhash: 123
B:do_configure
taskhash: ccc
unihash: ccc
B:do_populate_sysroot
taskhash: ddd
unihash: ddd
Notes: A:do_populate_sysroot executes
  It calculates the same outhash as before
  Reports the outhash and taskhash to the hash equivalence server
  The server stores off this hash in the database
  The server notes that there is an older matching taskhash in the database with the same output hash
  The server reports back to bitbake that the unihash for A:do_populate_sysroot should be changed to “222”

## Slide 32: Runqueue Execution with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot
taskhash: bbb
unihash: 222
B:do_configure
taskhash: 333
unihash: 333
B:do_populate_sysroot
taskhash: 444
unihash: 444
Notes: The change in the unihash for A:do_populate_sysroot prompts bitbake to re-calculate the task hashes for all downstream tasks
  Because the taskhash is based on the dependant’s unihash, these calculate to the values they previously held
  Importantly, the unihash for B:do_populate_sysroot now matches the hash for the cached sstate object

## Slide 33: Runqueue Execution with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot
taskhash: bbb
unihash: 222
B:do_populate_sysroot_setscene
taskhash: 444
unihash: 444
Notes: Bitbake realizes that it can restore B:do_populate_sysroot from cache sstate
  Executes B:do_populate_sysroot_setscene
  Completely skips B:do_configure
  In the traditional runqueue, this would not be allowed because bitbake can’t go back and execute setscene tasks
  The new runqueue does allow this though:
    Setsecene tasks are allowed to be added to the run queue at any time
    Anytime setsecene tasks are added, bitbake will execute them all, then continue with normal task execution
Questions about this process?

## Slide 34: Signature Generation with Hash Equivalence Server
Notes: Now we are going to look at what happens when bitbake generates signatures for the runqueue with the hashserver
  E.g. A clean build on another host, but has access to the hash server and sstate from previous example
Signature generation is the process where bitbake calculates the task hashes for tasks in the runqueue
  Occurs before any tasks execute
  Reported as part of the “Initializing tasks” line when running bitbake

## Slide 35: Signature Generation with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot
taskhash: bbb
unihash: 222
B:do_configure
taskhash: 333
unihash: 333
B:do_populate_sysroot
taskhash: 444
unihash: 444

## Slide 36: Signature Generation with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
Notes: A:do_configure task is initially calculated with the taskhash “aaa”

## Slide 37: Signature Generation with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot
taskhash: bbb
unihash: bbb
Notes: Bitbake initially calculates the taskhash and unihash for A:do_populate_sysroot as “bbb”

## Slide 38: Signature Generation with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot
taskhash: bbb
unihash: 222
Notes: After, it will query the hash server and ask if there is a better unihash for “bbb”
The server will consult the database and discover that “bbb” is equivalent to the older taskhash “222”
  b/c They have the same output hash
Bitbake will change the unihash for the task accordingly

## Slide 39: Signature Generation with Hash Equivalence Server
A:do_configure
taskhash: aaa
unihash: aaa
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot
taskhash: bbb
unihash: 222
B:do_configure
taskhash: 333
unihash: 333
B:do_populate_sysroot
taskhash: 444
unihash: 444
Notes: Parsing will continue with subsequent tasks
  Note that now the caches sstate tarballs can be used immediately since the unihash matches the cached tarball hashes before any tasks are run

## Slide 40: Signature Generation with Hash Equivalence Server
A:do_populate_sysroot:222
B:do_populate_sysroot:444
Hash server
outhash 123 = taskhash 222
outhash 123 = taskhash bbb
A:do_populate_sysroot_setscene
taskhash: bbb
unihash: 222
B:do_populate_sysroot_setscene
taskhash: 444
unihash: 444
Notes: Bitbake will execute the setsence tasks, never needing to execute the tasks with differing hashes
This is very powerful when sstate and the hash server are both shared
  It means that only one builder needs to to be the first to build and discover an equivalent hash
    After that, everyone else will detect the hashes as equivalent and restore from sstate
Questions?

## Slide 41: Live Demo & Exercise

## Slide 42: The Role of Reproducible Builds
Hash equivalence and reproducible builds go together
  Better reproducibility means better hash equivalence
Notes: Better build reproducibility means better hash equivalency
  Remember: equivalent hashes are determined by the outhash
    If the same build doesn’t generate the same outhash, it can’t be determined to be equivalent
Reproducibility is important for other reasons, hopefully hash equivalence helps drive it to be more important for everyone else!

## Slide 43: Alternative Output Hash Methods
The output hashing method can be replaced
Opportunity to implement context-sensitive hashes
  ELF Library Symbol hashing
  Scripting language specific hashing
  Locking hashes

## Slide 44: Activity Three
User Space Topics
Rudi Streif

## Slide 45
Overview
Activity Setup
Users, Groups and Passwords
Login Shells
Sudo Configuration
SSH Server Configuration
Please ask questions.
Your questions might help others too.

## Slide 46
Activity Setup
$ cd /scratch/poky
$ source oe-init-build-env build
$ bitbake-layers create-layer meta-activity3
NOTE: Starting bitbake server…
Add your new layer with ‘bitbake-layers add-layer meta-activity3’
$ bitbake-layers add-layer meta-activity3
NOTE: Starting bitbake server…
$ cat conf/bblayers.conf
…
BBLAYERS ?= “ \
/scratch/poky/meta \
/scratch/poky/meta-poky \
/scratch/poky/meta-yocto-bsp \
/scratch/poky/build/meta-activity3 \
“
Create an activity layer and add it to the build environment

## Slide 47
Activity Setup
$ mkdir -p meta-activity3/recipes-core/images
$ pushd meta-activity3/recipes-core/images
$ vi core-image-activity3.bb
Create an image recipe
SUMMARY = "Activity 3 Test Image"
DESCRIPTION = "Activity 3 Test Image for Yocto Project DevDay"
LICENSE = "MIT"
IMAGE_INSTALL = "packagegroup-core-boot \
packagegroup-base-extended \
${CORE_IMAGE_EXTRA_INSTALL} \
"
inherit core-image
$ bitbake core-image-activity3
$ runqemu qemuarm nographic

## Slide 48
Users, Groups and Passwords
The extrausers class provides a mechanism for managing users, groups and passwords.
Available commands:
  useradd
  usermod
  userdel
  groupadd
  groupmod
  groupdel
Commands are added to the EXTRA_USERS_PARAMS variable.
Passwords must be provided in encrypted form.

## Slide 49
Setting root user password and creating a user
$ vi core-image-activity3.bb
SUMMARY = "Activity 3 Test Image"
DESCRIPTION = "Activity 3 Test Image for Yocto Project DevDay"
LICENSE = "MIT"
IMAGE_INSTALL = "packagegroup-core-boot \
packagegroup-base-extended \
${CORE_IMAGE_EXTRA_INSTALL} \
"
inherit core-image
inherit extrausers
ROOT_PASSWORD = "secret"
DEV_PASSWORD = "hackme"
EXTRA_USERS_PARAMS = " \
groupadd developers; \
useradd -p `openssl passwd ${DEV_PASSWORD}` developer; \
useradd -g developers developer; \
usermod -p `openssl passwd ${ROOT_PASSWORD}` root; \
"
$ bitbake core-image-activity3
$ runqemu qemuarm nographic

## Slide 50
Works, but...
Changing the image recipe for new users is not really elegant.
It would be better if we could set the users we want to add and their passwords in a configuration file such as local.conf or a distro configuration.

## Slide 51
A little script goes a long way...
# Image post-processing to setup user accounts
inherit extrausers
# Space-delimited list of user:password:<group,group,...> tuples
NEWUSERS ??= ""
# root password
ROOT_PASSWORD ??= ""
python () {
params = ""
# add new users
newusers = (d.getVar("NEWUSERS", True) or "").split()
if newusers:
for user in newusers:
name,password,groups = user.split(":")
for group in groups.split(","):
params += "groupadd -f " + group + "; "
params += "useradd -p `openssl passwd " + password + "` "
if groups:
params += "-G " + groups + " "
params += name + "; "
# modify root password
rootpw = d.getVar("ROOT_PASSWORD", True) or ""
if rootpw:
params += "usermod -p `openssl passwd " + rootpw + "` root; "
d.setVar("EXTRA_USERS_PARAMS", params)
}
$ vi user-setup.inc

## Slide 52
Using the script
$ vi core-image-activity3.bb
$ vi /scratch/poky/build/conf/local.conf
# Users to be added: space-delimited list of name:password:groups tuples.
# groups is comma-delimited list of additional group names
NEWUSERS = "developer:hackme:developers"
# Root User Password
ROOT_PASSWORD = "secret"
SUMMARY = "Activity 3 Test Image"
DESCRIPTION = "Activity 3 Test Image for Yocto Project DevDay"
LICENSE = "MIT"
IMAGE_INSTALL = "packagegroup-core-boot \
packagegroup-base-extended \
${CORE_IMAGE_EXTRA_INSTALL} \
"
inherit core-image
require user-setup.inc
$ bitbake core-image-activity3
$ runqemu qemuarm nographic

## Slide 53
Image Post Processing
Sometimes it is necessary to processing such as adding, modifying files and more after the root file system has been created but before it is packaged into the different formats.
Through the variable ROOTFS_POSTPROCESS_COMMAND you can specify a list of shell functions to be executed.
Commonly the variable and the functions are added to the image recipe.
The functions are executed in the order they appear in the variable.
The search path for shell commands includes the native system root of the build environment and build host PATH from the user environment.
The variable IMAGE_ROOTFS points to the directory where the build system assembles the root file system.

## Slide 54
Setting Login Shells
$ vi core-image-activity3.bb
SUMMARY = "Activity 3 Test Image"
DESCRIPTION = "Activity 3 Test Image for Yocto Project DevDay"
LICENSE = "MIT"
IMAGE_INSTALL = "packagegroup-core-boot \
packagegroup-base-extended \
${CORE_IMAGE_EXTRA_INSTALL} \
"
inherit core-image
modify_shells() {
printf "# /etc/shells: valid login shells\n/bin/sh\n/bin/bash\n" \
> ${IMAGE_ROOTFS}/etc/shells
}
ROOTFS_POSTPROCESS_COMMAND += "modify_shells;"
$ bitbake core-image-activity3
$ runqemu qemuarm nographic

## Slide 55
Sudo Configuration
$ vi core-image-activity3.bb
SUMMARY = "Activity 3 Test Image"
DESCRIPTION = "Activity 3 Test Image for Yocto Project DevDay"
LICENSE = "MIT"
IMAGE_INSTALL = "packagegroup-core-boot \
packagegroup-base-extended \
${CORE_IMAGE_EXTRA_INSTALL} \
sudo \
"
inherit core-image
modify_sudoers() {
sed 's/# %sudo/%sudo/' < ${IMAGE_ROOTFS}/etc/sudoers > \
${IMAGE_ROOTFS}/etc/sudoers.tmp
mv ${IMAGE_ROOTFS}/etc/sudoers.tmp ${IMAGE_ROOTFS}/etc/sudoers
}
ROOTFS_POSTPROCESS_COMMAND += "modify_sudoers;"
$ bitbake core-image-activity3
$ runqemu qemuarm nographic
Note: You have to add a regular user to the sudo group for this to work.

## Slide 56
SSH Server Configuration
$ vi core-image-activity3.bb
configure_sshd() {
# disallow password authentication
echo “PasswordAuthentication no” >> ${IMAGE_ROOTFS}/etc/ssh/sshd_config
# create keys in tmp/deploy/keys
mkdir -p ${DEPLOY_DIR}/keys
if [ ! -f ${DEPLOY_DIR}/keys/root-sshkey ]; then
/usr/bin/ssh-keygen -t rsa -N '' \
-f ${DEPLOY_DIR}/keys/root-sshkey
fi
# add public key to authorized_keys for root
mkdir -p ${IMAGE_ROOTFS}/home/root/.ssh
cat ${DEPLOY_DIR}/keys/root-sshkey.pub \
>> ${IMAGE_ROOTFS}/home/root/.ssh/authorized_keys
}
ROOTFS_POSTPROCESS_COMMAND += "configure_sshd;"
$ bitbake core-image-activity3
$ runqemu qemuarm nographic
[in a new ssh shell to your build system]
$ ssh -i \
/scratch/poky/build/tmp/deploy/keys/root-sshkey root@192.168.7.2

## Slide 57
Nice, but once again not very flexible...
$ vi sshd-setup.inc
# Image post-processing to configure sshd
# Setup ssh key login for these users
SSH_USERS ??= ""
configure_sshd() {
# disallow password authentication
echo "PasswordAuthentication no" >> ${IMAGE_ROOTFS}/etc/ssh/sshd_config
# keys will be stored tmp/deploy/keys
mkdir -p ${DEPLOY_DIR}/keys
# create the keys for the users
for user in ${SSH_USERS}; do
if [ ! -f ${DEPLOY_DIR}/keys/${user}-sshkey ]; then
/usr/bin/ssh-keygen -t rsa -N '' \
-f ${DEPLOY_DIR}/keys/${user}-sshkey
fi
# add public key to authorized_keys for the user
mkdir -p ${IMAGE_ROOTFS}/home/${user}/.ssh
cat ${DEPLOY_DIR}/keys/${user}-sshkey.pub \
>> ${IMAGE_ROOTFS}/home/${user}/.ssh/authorized_keys
done
}
ROOTFS_POSTPROCESS_COMMAND += "configure_sshd;"

## Slide 58
Using the script
$ vi core-image-activity3.bb
$ vi /scratch/poky/build/conf/local.conf
# Users for whom to create ssh login with key
SSH_USERS = "root developer"
SUMMARY = "Activity 3 Test Image"
DESCRIPTION = "Activity 3 Test Image for Yocto Project DevDay"
LICENSE = "MIT"
IMAGE_INSTALL = "packagegroup-core-boot \
packagegroup-base-extended \
${CORE_IMAGE_EXTRA_INSTALL} \
"
inherit core-image
require sshd-setup.inc
$ bitbake core-image-activity3
$ runqemu qemuarm nographic
[in a new ssh shell to your build system]
$ ssh -i \
/scratch/poky/build/tmp/deploy/keys/developer-sshkey \
developer@192.168.7.2

## Slide 59
EoA (End of Activity)
Cleanup
Thank You!
$ cd /scratch/poky/build
$ bitbake-layers remove-layer meta-activity3

## Slide 60: Activity Four
On Target Development using Package Feeds
Stephano Cetola

## Slide 61: Package Manager Overview

## Slide 62: Yocto Package Feed Overview
Tested package types: rpm and ipk
For rpm packages, we now use DNF
Setting up a package feed is EASY
  stephano.cetola@linux.intel.com
  @stephano approves this message
Signing your packages and package feed is supported
Two major use cases:
  On target development (faster and smarter)
  In the field updates (YMMV)

## Slide 63: Understanding RPM Packages in Yocto
RPMs located in: tmp/deploy/rpm/ARCH/
<blink>index database NOT CREATED YET</blink>

## Slide 64: Understanding RPM Package Index in Yocto
Running “bitbake package-index” generates the db:
$ ls tmp/deploy/rpm/qemux86/repodata
[bunch of sqlite files]
repomd.xml
$ cat repomd.xml
<?xml version="1.0" encoding="UTF-8"?>
<repomd xmlns="http://linux.duke.edu/metadata/repo">
<revision>1566265277</revision>¬
<data type="primary">¬
<checksum type="sha256">2336fe2c…d0f</checksum>¬
<open-checksum type="sha256">db11…d9e4e9a</open-checksum>
<location href="repodata/2336…f27de1d0f-primary.xml.gz"/>
<timestamp>1566265277</timestamp>
<size>68850</size>
<open-size>998064</open-size>
</data>

## Slide 65: Tools and Commands
Repository Tools
  createrepo
  rpm2cpio
  dnf (replaces yum)
  yum-utils (historical)
Important Commands
  rpm -qip (general info)
  rpm -qpR (depends)
  https://wiki.yoctoproject.org/wiki/TipsAndTricks/UsingRPM

## Slide 66: Tools and Commands
Getting general info:
$ rpm -qip xserver-xf86-config-0.1-r33.0.qemux86.rpm
Name : xserver-xf86-config
Version : 0.1
Release : r33.0
Architecture: qemux86
Group : x11/base
Size : 1165
License : MIT-X
Source RPM : xserver-xf86-config-0.1-r33.0.src.rpm
Build Date : Thu 11 Apr 2019 05:09:21 PM PDT
Packager : Poky poky@yoctoproject.org (see: MAINTAINER var)
URL : http://www.x.org
Summary : X.Org X server configuration file
Description : X.Org X server configuration file.

## Slide 67: On Target Development – Better, Faster, Stronger
Topics
  Setting up a package feed
  Using PR Server
  Signing package feeds
  Keeping your code secure
  The future of package feeds

## Slide 68: Setting up a package feed - Target Setup
Install Package Management on the target
  EXTRA_IMAGE_FEATURES += " package-management "
Set the correct package class
  PACKAGE_CLASSES = "package_rpm”
Customize the feed (optional)
  PACKAGE_FEED_URIS = http://my-server.com/repo
  PACKAGE_FEED_BASE_PATHS = "rpm”
  PACKAGE_FEED_ARCHS = ”all armv7at2hf-neon beaglebone"
Edit /etc/yum.repos.d/oe-remote-repo.repo (optional)
  enabled=1
  metadata_expire=0
  gpgcheck=0

## Slide 69: Setting up a package feed
Publish a repo, index the repo, and…
You are now running a web server on port 5678
$ bitbake core-image-minimal (or bitbake world)
...
$ bitbake package-index
...
$ twistd -n web --path tmp/deploy/rpm -p 5678
[-] Log opened
[-] twistd 16.0.0 (/usr/bin/python 2.7.12) starting up.
[-] reactor class: twisted.internet.epollreactor.EPollReactor.
[-] Site starting on 5678

## Slide 70: Caveats and Reminders
Running bitbake world can take some time
  You may want to update your repo as needed
Serve the repo from a build machine
  Or simply rsync to a webserver
Do not forget to run `bitbake package-index`
  Package index will not auto-update
Good practice is to dogfood your repo

## Slide 71: On Target Development – Better, Faster, Stronger
Topics
  Setting up a package feed
  Using PR Server
  Signing package feeds
  Keeping your code secure
  The future of package feeds

## Slide 72: Package Revision (PR) Server Overview
Allows package feeds to act as expected
Allows package feed consumers to get latest builds
Works with SigGen to know when things change
Versions increase in a linear fashion
Ordered by decreasing priority
PE, PV and PR **
**more on these later, see also:
https://wiki.yoctoproject.org/wiki/PR_Service

## Slide 73: PR Server Overview - Variables
PE – Epoch – Defaults to UNSET
PV – Version – Defaults to filename (recipe_2.0.1.bb)
  Recipes won’t touch this (unless building unstable)
PR – Revision – Defaults to r0
  When PV increases, PR is reset to ‘r0’
mega-manual -> #working-with-a-pr-service

## Slide 74: PR Server Example
Enable the server:
bitbake will stop and start the server
For complex setups use `bitbake-prserv`
It is recommended to use buildhistory (sanity checks)
PRSERV_HOST = "localhost:0"
INHERIT += "buildhistory“
BUILDHISTORY_COMMIT = "1"

## Slide 75: PR Server - Commands
bitbake-prserv – Start, stop, edit server properties
bitbake-prserv-tool – Export & Import PRs
#Table: PRMAIN_nohist
#Columns:
#name type notn dflt pk
#---------- -------- -------- -------- ----
# version TEXT 1 None 1
# pkgarch TEXT 1 None 1
# checksum TEXT 1 None 1
# value INTEGER 0 None 0
# Exported Per-recipe data example
PRAUTO$zlib-1.2.7-r0$i586$fae8ba2c781fd378307f4a90c021a798 = "0"
PRAUTO_zlib-1.2.7-r0_i586 = "0"
PRAUTO$ncurses-5.9-r13.1$i586$4bcaad698464a6db2f1555aa2327ff = "0"
PRAUTO_ncurses-5.9-r13.1_i586 = "0"

## Slide 76: On Target Development – Better, Faster, Stronger
Topics
  Setting up a package feed
  Using PR Server
  Signing package feeds
  Keeping your code secure
  The future of package feeds

## Slide 77: Signing Overview
This is not “required”
Unnecessary in a closed network (i.e. machine local)
Any LAN is unsecure
Without GPG, package feeds are unencrypted traffic
LMGTFY: Zero Trust Environment
Should be obvious for package feeds over WAN

## Slide 78: Signing The Packages
Inherit bbclass to enable signing functionality
  INHERIT += “sign_rpm”
Define the GPG key that will be used for signing.
  RPM_GPG_NAME = "key_name”
Provide passphrase for the key
  RPM_GPG_PASSPHRASE = "passphrase"

## Slide 79: Signing The Package Feed
Inherit bbclass to enable signing functionality
  INHERIT += “sign_package_feed”
Define the GPG key that will be used for signing.
  PACKAGE_FEED_GPG_NAME = "key_name”
Provide passphrase for the key
  PACKAGE_FEED_GPG_PASSPHRASE_FILE = "passphrase"

## Slide 80: Signing The Package Feed (optional)
GPG_BIN
  GPG binary executed when the package is signed
GPG_PATH
  GPG home directory used when the package is signed.
PACKAGE_FEED_GPG_SIGNATURE_TYPE
  Specifies the type of gpg signature. This variable applies only to RPM and IPK package feeds. Allowable values for the PACKAGE_FEED_GPG_SIGNATURE_TYPE are "ASC", which is the default and specifies ascii armored, and "BIN", which specifies binary.

## Slide 81: Testing Packages with ptest (Optional? Not really!)
Package Test (ptest)
  Runs tests against packages
  Contains at least two items:
    the actual test (can be a script or an elaborate system)
    shell script (run-ptest) that starts the test (not the actual test)
Simple Setup
  DISTRO_FEATURES_append = " ptest”
  EXTRA_IMAGE_FEATURES += "ptest-pkgs”
  Installed to: /usr/lib/package/ptest

## Slide 82: On Target Development – Better, Faster, Stronger
Topics
  Setting up a package feed
  Using PR Server
  Signing package feeds
  Keeping your code secure
  The future of package feeds

## Slide 83: Keeping feeds secure
PACKAGE_FEED_GPG_PASSPHRASE_FILE
  This should NOT go in your configuration as plain text.
Is your code proprietary?
  You should probably be shipping a binary in Yocto
  bin_package.bbclass: binary can be .rpm, .deb, .ipk
Have you thought about DEBUG_FLAGS?
  See bitbake.conf for more details
  The flags can be filtered or set in the recipe

## Slide 84: On Target Development – Better, Faster, Stronger
Topics
  Setting up a package feed
  Using PR Server
  Signing package feeds
  Keeping your code secure
  The future of package feeds

## Slide 85: The Future of Package Feeds – Can We Upgrade?
Repository
  Switch to new source entries
  Remove unknown (3rd party) repositories
Package
  Check there are no broken or renamed packages
  Versioning: what happens when they go backwards
  Remove and install specific packages (release dependent)
  Remove blacklisted / obsolete and add whitelisted
Dreaming Even Bigger…
  Kernels, Desktops (UI), Permissions, Users, Groups

## Slide 86: Yocto as a Binary Distro
Yocto Project provides SSTATE, why not Package Feeds?
  What would be our scope?
  What target machines would we ship?
  What versions would we support?
  How would we deploy a test infrastructure?

## Slide 87: Yocto as a Binary Distro – Questions to Answer
What would be our scope?
  Open Embedded Core
  Specific meta-oe layers
  Specific layers from layers.openembedded.com

## Slide 88: Yocto as a Binary Distro – Questions to Answer
What target machines would we ship?
  QEMU, hardware, or both
  X86-64, ARM, MIPS, PPC
  If PPC / MIPS, who supports them?

## Slide 89: Yocto as a Binary Distro – Questions to Answer
What versions would we support?
  Rolling Release
  CVE fixes only
  Last 2 Major Versions
  Minor Versions for CVEs only
  Inherent need for Long Term Support (LTS)

## Slide 90: Yocto as a Binary Distro – Questions to Answer
How would we deploy a test infrastructure?
  ptests required
  Support rollback
  Fail gracefully
  eSDK
  Community supported

## Slide 91: Activity Five A
Mirrors and SState
David Reyna

## Slide 92: Mirrors and Pre-Mirrors
MIRRORS specifies additional paths from which the build system gets source code. When the build system searches for source code, it first tries the local download directory. If that location fails, the build system tries locations defined by PREMIRRORS, the upstream source, and then locations specified by MIRRORS in that order.
PREMIRROR is a set of rules applied to URIs prior to fetching. The rules are composed of an RE followed by a substitution rule.
BB_ALLOWED_NETWORKS specifies a space-delimited list of hosts that the fetcher is allowed to use to obtain the required source code, with limited RE support, for example: BB_ALLOWED_NETWORKS = "*.gnu.org"
BB_NO_NETWORK disables network access in the BitBake fetcher modules. With this access disabled, any command that attempts to access the network becomes an error.

## Slide 93: Uses for pre-mirrors
No Network Access
  When you need to completely lock out external content, either for security reasons or code contamination reasons, you can use BB_NO_NETWORKS.
Limited Network Access
  When you want to allow only certain network paths, internal and/or external, for example to manage development repositories, you can use BB_ALLOWED_NETWORKS.
Managed and Redirected Network Access
  When you want to allow substitutions of networks when and if they are available, for example to access internal repositories when in the factory and then public repositories when in the field, you can use PREMIRROR.
Protocol Swaps
  When you want to substitute potentially blocked repository ports with un-blocked ports, for example swap git access for HTTP access, using the RE features of PREMIRROR.

## Slide 94: How PREMIRROR RE substitution works
The URL parser decodes an URL into tokens, specifically “scheme”, “network location”, “path”, “user”, “password”, and “parameters”
The parser will then match the set of PREMIRROR’s rules with the URL on a per token basis.
The parser will then repeat PREMIRROR’s rules matching on this new set of URLs. This repeats until no more matches are found.
The result will be a list of the original URLs together with all of the recursive matches.
Example of a complex rule:
git://.*/.*/(.*) https://${CORP_MIRRORS}/gadget/oe-core-dl-1.8/${CORP-MIRRORS-SHOW-BRANCH}:downloads/\1

## Slide 95: Infinite PREMIRROR Loop Example
The bad news is this facility can lead to infinite loops that can overrun python and even your disk. The good news is this has been fixed since Yocto Project 2.0. The bad news is that it could still happen to you.
Example Rules:
git://.*/.* http://A/A_
http://.*/.* http://B/B_
Let us begin (without fix in 2.0):
git://a.b.com/foo.git -> http://A/A_foo.git
http://A/A_foo.git -> http://B/B_A_foo.git
http://B/B_A_foo.git -> http://B/B/B_B_A_foo.git
(loop!)

## Slide 96: PREMIRROR Advice
Design your rules so that a conversion rule does not match itself. Here is an example of a set of rules that explicitly blocks self-matching after the first substitution: git://.*/.*/(.*) https://${CORP_MIRRORS}/gadget/oe-core-dl-1.8/${CORP_MIRRORS_SHOW_BRANCH}:downloads/\1 https://^(?!${CORP_MIRRORS}).*/.* https://${CORP_MIRRORS}/gadget/oe-core-dl-1.8/${CORP_MIRRORS_SHOW_BRANCH}:/
However, with that said, there still can be implicit loops, such that one rule will run over the results of a previous rule.
And of course it's the sum of PREMIRRORS, <regular>, MIRRORS in the download order. The more rules you put in, the bigger the table, the more matching attempts may be processed before a non-match.

## Slide 97: PREMIRROR
There is a regression test under “bitbake/lib/bb/tests” that is run to see if the distribution as the issue.
Here is that test’s output. It does show that the recursion is fixed. Surprisingly, it also showed an extra conversion that was not expected!
recmirrorvar = "https://.*/[^/]* http://AAAA/A/A/A/ \n" \
"https://.*/[^/]* https://BBBB/B/B/B/ \n"
def test_recursive(self):
fetcher = bb.fetch.FetchData("https://downloads.yoctoproject.org/releases/bi
tbake/bitbake-1.0.tar.g$
mirrors = bb.fetch2.mirror_from_string(self.recmirrorvar)
uris, uds = bb.fetch2.build_mirroruris(fetcher, mirrors, self.d)
self.assertEqual(uris, ['http://AAAA/A/A/A/bitbake/bitbake-1.0.tar.gz',
'https://BBBB/B/B/B/bitbake/bitbake-1.0.tar.gz',

## Slide 98: Sstate and Downloads
SSTATE
  Each build has a sstate-cache directory that collects the generated packages. The build will look in this directory first to avoid unnecessary rebuilding of otherwise unchanged packages
  In the name of each cached file contains a checksum string, known as the signature. The signature is a calculated sum of identifying dependence artifacts that track if the package source has changed. When the calculated sum matches a cached sum, the cached content is reused, else the package is re-built (and ends up with a new checksum)
Downloads
  Each build also has a download directory, where all source packages that are not local are copied and placed
  For the download directory, uniqueness is determined by the source package's name, which normally have version information

## Slide 99: Sstate and Downloads: Sharing and Portability
The sstate and download directories can be shared between projects, allowing the work of one project save time for the other projects. This is done by setting the SSTATE_DIR and the DL_DIR values in each project to common external directories.
The sstate and download directories can be shared across networks, for example across an NFS mount.
The sstate and download directories are portable, meaning that it can be copied from one machine to another.
The sstate-cache is access-rights safe between users. The bitbake required umask of 022 insures that all such files are readable by all other users.
Notes: Implicit in these features is for example the requirement that the signature computation does not include things like absolute paths.

## Slide 100: Sstate: Mirrors
What we learned about Mirrors can apply Sstate
SSTATE_MIRRORS
  Configures the build system to search other mirror locations for prebuilt cache data objects before building out the data. This variable works like fetcher MIRRORS and PREMIRRORS and points to the cache locations to check for the shared objects.
SSTATE_MIRROR_ALLOW_NETWORK
  If set to "1", allows fetches from mirrors that are specified in SSTATE_MIRRORS to work even when fetching from the network has been disabled by setting BB_NO_NETWORK to "1". Using the SSTATE_MIRROR_ALLOW_NETWORK variable is useful if you have set SSTATE_MIRRORS to point to an internal server for your shared state cache, but you want to disable any other fetching from the network.
Notes: Implicit in these features is for example the requirement that the signature computation does not include things like absolute paths.

## Slide 101: Sstate: recommendations
In complex systems it is recommended to separate sstate directories, for example native and non-native sstate directories, and also different BSPs and arches.
Reusing a single directory will grow very large very quickly. Use atime to delete old files. Note: this requires the filesystem mounted with atime/relatime which we normally recommend to disable for build performance. find ${sstate_dir} -name 'sstate*' -atime +3 -delete; fi
Rebuild sstate to new directory periodically and delete old sstate dir to maintain bounded size. There may be packages or package versions that are no longer used and just take up space.
Although it is possible to use other protocols for the sstate such as HTTP and FTP, you should avoid these. Using HTTP limits the sstate to read-only and FTP provides poor performance.
Additionally, a missing sstate file on http/ftp server cause wget to hang for a long time due to the retries and timeout

## Slide 102: Sstate: Known issues
A new changeset may invalidate part or all of the sstate cache occasionally - this is by design
Native package’s sstate-cache can’t be reused among 32-bit and 64-bit host
Native sstate dependent on glibc version and native sstate compiled with newer glibc version cannot be used on systems with older glibc
The calculated signatures are not always perfect. For example, if a recipe copies files directly into its install directory and those files are not otherwise registered in the FILES directive, any file changes will be invisible to the signature, and even though the package builds the image will be populated by the original sstate version
Users with different PR Servers can cause package extra-version incrementing that is inconsistent, resulting in false wins
Never the less, the sstate-cache feature will save you a tremendous amount of time, and it has proven to be very stable. Use it!

## Slide 103: Debugging Sstate Issues
There are two important tools to help debug sstate issues
Build History: tells you ‘what’ changed
bitbake-diffsigs: helps you figure out the 'why‘
Build History
  The buildhistory class exists to help you maintain the quality of your build output. You can use the class to highlight unexpected and possibly unwanted changes in the build output. When you enable build history, it records information about the contents of each package and image and then commits that information to a local Git repository where you can examine the information.
bitbake-diffsigs
  This tool is a BitBake task signature data comparison utility
  You can use this tool to check any changes between sstate cache and new produced one.

## Slide 104: Debugging Sstate Issues
Build History
  Enabling: build history is disabled by default. To enable it, add the following at the end of your conf/local.conf file:
INHERIT += "buildhistory“ BUILDHISTORY_COMMIT = "1“
  The build history information is kept in BUILDHISTORY_DIR , generally equal to “${TOPDIR}/buildhistory”
  The directory tracks build information into image, packages, and SDK subdirectories.
bitbake-diffsigs
  The usage is: bitbake-diffsigs -t recipename taskname bitbake-diffsigs sigdatafile1 sigdatafile2 bitbake-diffsigs sigdatafile1
    The signature files are in the stamps directory, for example: tmp/stamps/armv5e-poky-linux-gnueabi/busybox/*sig*

## Slide 105: Activity Five B
WIC
Eduard Bartosh, David Reyna

## Slide 106: WIC: Open Embedded Image Creation
Physical devices accept and boot images in various ways depending on the specifics of the device. If your device require multiple partitions on an SD card, flash, or an HDD, you can use wic to create the properly partitioned image.
The wic command generates partitioned images from existing OpenEmbedded build artifacts.
Image generation is driven by partitioning commands contained in an provided or custom Openembedded kickstart file (.wks)
The wic was designed to be completely extensible through a plug-in interface

## Slide 107: WIC: Requirements
You need to have the build artifacts already available, e.g. created an image like "core-image-minimal"
You must build several native tools, which are tools built to run on the build system: $ bitbake parted-native dosfstools-native mtools-native
You must have sourced one of the build environment setup scripts (i.e. oe-init-build-env or oe-init-build-env-memres)

## Slide 108: WIC: Help
Wic is documented on-line here: https://www.yoctoproject.org/docs/latest/mega-manual/mega-manual.html#creating-partitioned-images-using-wic
You can get help from wic, where the available commands and help topics $ wic –h $ wic --help
The wic help lists the available commands and help topics, from which you can request deeper help information $ wic help command $ wic help help_topic

## Slide 109: WIC: Help
You can find out more about the images wic creates using the existing kickstart files with the following form of the command, where image is either "directdisk" or "mkefidisk"
$ wic list image help

## Slide 110: WIC: Operational Modes
You can use wic in two different modes, depending on how much control you need for specifying the Openembedded build artifacts that are used for creating the image: Raw and Cooked:
  Raw Mode: You explicitly specify build artifacts through command-line arguments.
  Cooked Mode: The current MACHINE setting and image name are used to automatically locate and provide the build artifacts.
You do not need root privileges to run wic. In fact, you should not run as root when using the utility.

## Slide 111: WIC: Cooked Mode
The general form of the wic command using Cooked Mode is: $ wic create kickstart_file -e image_name
  kickstart_file: An OpenEmbedded kickstart file. You can provide your own custom file or supplied file.
  image_name: Specifies the image built using the OpenEmbedded build system.
Example: $ wic create mkefidisk -e core-image-minimal

## Slide 112: WIC: Raw Mode
The general form of the 'wic' command in raw mode is: $ wic create image_name.wks [options] [...]
Where: image_name.wks (An OpenEmbedded kickstart file) -o OUTDIR, --outdir=OUTDIR -e IMAGE_NAME, --image-name=IMAGE_NAME -r ROOTFS_DIR, --rootfs-dir=ROOTFS_DIR -b BOOTIMG_DIR, --bootimg-dir=BOOTIMG_DIR -k KERNEL_DIR, --kernel-dir=KERNEL_DIR -n NATIVE_SYSROOT, --nativesysroot=NATIVE_SYSROOT -s, --skip-build-check -D, --debug
Example: $ wic create directdisk -r rootfs_dir -b bootimg_dir \ --k kernel_dir -n native_sysroot

## Slide 113: WIC: Available kickstart files
You can use wic to get a list of available kickstarts
$ wic list images
beaglebone-yocto SD card image for Beaglebone
genericx86 EFI disk image for genericx86*
edgerouter SD card image for Edgerouter
mpc8315e-rdb SD card image for MPC8315E-RDB
mkhybridiso Hybrid ISO image
sdimage-bootpart SD card image w/ boot partition
directdisk-gpt 'pcbios' direct disk image
systemd-bootdisk EFI disk image with systemd-boot
directdisk 'pcbios' direct disk image
qemux86-directdisk qemu machine 'pcbios' direct disk
directdisk-bootloader-config 'pcbios' direct disk image
with custom bootloader config
directdisk-multi-rootfs multi rootfs image w/ rootfs plugin
mkefidisk EFI disk image$

## Slide 114: WIC: Example Kickstart File
Here is the “mkefidisk.wks” kickstart file
# short-description: Create an EFI disk image
# long-description: Creates a partitioned EFI disk image that user
# can directly dd to boot media.
part /boot --source bootimg-efi --ondisk sda --label msdos \
--active --align 1024
part / --source rootfs --ondisk sda --fstype=ext3 \
--label platform --align 1024
part swap --ondisk sda --size 44 --label swap1 --fstype=swap
bootloader --timeout=10 --append="rootwait rootfstype=ext3 \
console=ttyPCH0,115200 console=tty0 vmalloc=256MB \
snd-hda-intel.enable_msi=0"

## Slide 115: WIC: Using WIC (genericx86)
$ wic create mkefidisk -e core-image-minimal
INFO: Building wic-tools...
...
INFO: The new image(s) can be found here:
./mkefidisk-201804191017-sda.direct
The following build artifacts were used to create the image(s):
ROOTFS_DIR: /.../build/tmp-glibc/work/genericx86-oe-lin...
BOOTIMG_DIR: /.../build/tmp-glibc/work/genericx86-oe-lin...
KERNEL_DIR: /.../build/tmp-glibc/deploy/images/genericx86...
NATIVE_SYSROOT: /.../build/tmp-glibc/work/i586-oe-linux/...
INFO: The image(s) were created using OE kickstart file:
/home/user/master/openembedded-core/scripts/lib/wic/canned-wks/
mkefidisk.wks
$ sudo dd if=/var/tmp/wic/build/mkefidisk-201804191017-sda.direct \
of=/dev/sdb bs=1M
$ sudo eject /dev/sdb

## Slide 116: WIC: Custom Kickstart Files
You can create your own custom kickstart and easily have wic find and use them. See the WIC documentation.
Existing kickstart files can be found here, and used as templates: poky/scripts/lib/image/wic/canned-wks
You can place your custom kickstart file with the canned ones, or add it to your layer
Currently wic implementation only supports "partition" and "bootloader“ (more to come). See also: http://fedoraproject.org/wiki/Anaconda/Kickstart#part_or_partition http://fedoraproject.org/wiki/Anaconda/Kickstart#bootloader

## Slide 117: WIC: Plug-ins
Plug-ins allow wic functionality to be extended and specialized by users.
Source plug-ins provide a mechanism to customize various aspects of the image generation process in wic, mainly the contents of partitions.
The plug-ins provide a mechanism for mapping values specified in .wks files using the --source keyword to a particular plugin implementation that populates a corresponding partition.
Plug-ins can be included as part of your custom layer.
See the documentation for detailed information and examples.

## Slide 118: WIC:
Wic files can be automatically generated by adding WKS_FILE to your “local.conf”
New kickstart commands are being added by demand, for example “include” and “config”
We invite you to add kickstart files to your BSP layers for fast and easy OOB for your users

## Slide 119: Introducing BMAPTOOL : Sparse Boot Images
The new BMAPTOOL creates sparse images for fast image disk create (dd copies all of the blank space)
You can write images by using “bmaptool”: $ oe-run-native bmaptool copy mkefidisk-201804191017-sda.direct /dev/sdX
… or “dd”: $ sudo dd if=mkefidisk-201804191017-sda.direct of=/dev/sdX
Documentation for BMAPTOOL can be found here: https://www.yoctoproject.org/docs/latest/mega-manual/mega-manual.html#flashing-images-using-bmaptool
Here is information about bmap-tools Ubuntu package: http://packages.ubuntu.com/xenial/bmap-tools
And about the tool itself: https://github.com/01org/bmap-tools/tree/master/docs

## Slide 120: Activity Six
Container building/Multiconfig
Scott Murray

## Slide 121: Topics
Brief containers overview
Container support in OpenEmbedded / Yocto Project
Example OE/YP container configurations
Multiconfig
Containers and multiconfig?

## Slide 122: Caveats
This is an evolution of a previous talk at ELCE 2018
I am not a container expert, and this presentation does not cover the mechanics of using the discussed container images in detail
Container technology is progressing rapidly, it’s entirely possible I’ve missed something of interest (Please let me know!)
An intermediate level of OpenEmbedded / Yocto Project knowledge is assumed

## Slide 123: Containers
Operating system level virtualization as opposed to virtual machines
Linux implementations typically are based on namespaces and cgroups
  LXC, Docker, runc, systemd-nspawn
Newer Clear / Kata containers are based on lightweight VM technology
Container images can be full Linux distribution installs, or small images containing a single application and its dependencies

## Slide 124: Containers (continued)
Common use cases:
  Running an application that has incompatible dependencies from the host machine
  Sandboxing an application to isolate it from the host machine
  Implementing microservices where application containers are started based on demand
Typical container construction
  Start with a minimal Debian, Ubuntu, or Alpine Linux image
  Add required packages
  Potentially compile non-upstream available packages (e.g. via Dockerfile commands)
  Prune container down by removing unneeded files
            Small size is very desirable
            Reduces security attack surface, maintenance, and migration time

## Slide 125: Container Drawbacks?
Reproducibility
  Base containers changes may not be obvious, e.g Docker labels may change
  Package versions on Debian, Alpine, etc. changing
            It’s not uncommon to see “apt-get update && apt-get upgrade -y”, etc. in Dockerfiles
            Pinning package versions can break if the base distro doesn’t archive older versions
  Even if automating with Dockerfile(s) or other scripting, effort required to ensure result is reproducible
Transparency / Security
  You have to trust the builders of the base container
  Security is dependent on the providers of the base container, i.e. distribution update policies
  Often quoted problem of library updates potentially affecting many containers

## Slide 126: Container Drawbacks? (continued)
License compliance scheme
  Potentially can be pulled from package manager, but no particularly turn-key solutions
Customization
  Patching a package or tweaking its configuration flags requires manual or scripted rebuild
  Building for an unsupported architecture requires delving into the distribution’s build process

## Slide 127: So is OE / YP a solution?
Reproducibility
  Image builds can be straightforwardly reproduced using fixed metadata
Transparency / Security
  Entire build process is bootstrapped from scratch
  Typically 18 months support per release versus 5 years for Debian stable, ~2 years for Alpine
License compliance scheme
  Image license manifests and license text archiving
  Source archiving
Customization
  Layered metadata and build process allows adding almost any customization
  Any architecture with a BSP layer can be targeted

## Slide 128: So is OE / YP a solution? (continued)
Package availability
  Debian, Ubuntu several 10’s of K, Alpine ~5K
  OE ~2300 in oe-core and meta-openembedded, many more in other layers
  OE node.js and Python module availability is not as broad
Ease of use
  It take some work to reproduce something like the apt-get, apk install user experience with an OE built package feed
  Small, relatively fixed content images are going to be easier to handle
Resources
  OE is a new toolset to learn potentially
  Building images can require significant hardware resources
  Long term maintenance may involve dedicating resources

## Slide 129: OE / YP container support
Container image type
  Added in pyro / 2.3 release
  IMAGE_FSTYPES = “container”
  Produces a tar.bz2 with no kernel components or post-install scripts
  Requires PREFERRED_PROVIDER_virtual/kernel to be set to “dummy”
meta-virtualization layer
  LXC, runc, Docker (currently 18.09.3 in warrior, 19.03.0-rc3 in master)
  Open Container Initiative (OCI) image tools
  OCI image build support (based on skopeo) since warrior
  Kernel configuration fragments for linux-yocto
Currently no support for building LXC or Docker images during OE build
  Difficult with Docker itself, since it needs its daemon running
  LXC may be possible with lxc-create template hacking

## Slide 130: OE / YP container support (continued)
Togán Labs’ Oryx Linux
  Commercially supported OE based distribution
  Container support using runc on target
  https://www.toganlabs.com/oryx-linux/

## Slide 131: Examples
Build bootstrap container
  Contains the tools to run OE / YP builds, i.e. self-hosting
  Lighter container version of build-appliance VM image
Alpine-like container image
  Attempt to match base Alpine contents and size
Application container image
  Typical single application sandbox / microservice

## Slide 132: Build Bootstrap Container Example

## Slide 133: Quick and dirty with local.conf
MACHINE = “qemux86-64”
IMAGE_FSTYPES = "container"
PREFERRED_PROVIDER_virtual/kernel = "linux-dummy"
IMAGE_LINGUAS_append = " en-us"
CORE_IMAGE_EXTRA_INSTALL += " \
packagegroup-self-hosted-sdk \
packagegroup-self-hosted-extended \
"

## Slide 134: Notes
Resulting core-image-minimal for qemux86-64 is ~150 MB
Builds some graphical packages that go unused
Further tinkering required to prune out some things
Lack of post-install scripts means volatile directories (/var/volatile/*, etc.) do not get created
  Can run /etc/rcS.d/S37populate-volatile.sh
  Fixable with ROOTFS_POSTPROCESS or bbappend to base-files and fsperms.txt tweaking
User for building needs to be created / managed
Access to build tree needs to be managed
  Docker volume(s), mounts, etc.

## Slide 135: Image definition: build-container.bb
SUMMARY = "A minimal bootstrap container image"
IMAGE_FSTYPES = "container"
inherit core-image
IMAGE_INSTALL = " \
packagegroup-core-boot \
packagegroup-self-hosted-sdk \
packagegroup-self-hosted-extended \
${CORE_IMAGE_EXTRA_INSTALL} \
"
IMAGE_LINGUAS = "en-us"
# Workaround /var/volatile for now
ROOTFS_POSTPROCESS_COMMAND += "rootfs_fixup_var_volatile ; "
rootfs_fixup_var_volatile () {
install -m 1777 -d ${IMAGE_ROOTFS}/${localstatedir}/volatile/tmp
install -m 755 -d ${IMAGE_ROOTFS}/${localstatedir}/volatile/log
}

## Slide 136: Alpine-like Container Example

## Slide 137: Quick and dirty with local.conf
MACHINE = “qemux86-64”
IMAGE_FSTYPES = "container"
PREFERRED_PROVIDER_virtual/kernel = "linux-dummy"
TCLIBC = “musl”

## Slide 138: Resulting core-image-minimal manifest
base-files qemux86_64 3.0.14
base-passwd core2_64 3.5.29
busybox core2_64 1.30.1
busybox-hwclock core2_64 1.30.1
busybox-syslog core2_64 1.30.1
busybox-udhcpc core2_64 1.30.1
eudev core2_64 3.2.7
init-ifupdown qemux86_64 1.0
initscripts core2_64 1.0
initscripts-functions core2_64 1.0
libblkid1 core2_64 2.32.1
libkmod2 core2_64 26
libuuid1 core2_64 2.32.1
libz1 core2_64 1.2.11
modutils-initscripts core2_64 1.0
musl core2_64 1.1.21+git0+43e7efb465
netbase core2_64 5.6
packagegroup-core-boot qemux86_64 1.0
sysvinit core2_64 2.88dsf
sysvinit-inittab qemux86_64 2.88dsf
sysvinit-pidof core2_64 2.88dsf
update-alternatives-opkg core2_64 0.4.0
update-rc.d noarch 0.8
v86d qemux86_64 0.1.10

## Slide 139: Notes
Resulting core-image-minimal for qemux86-64 is ~4.8 MB
  ~8.5 MB with package management support via opkg
  Almost 100 MB with package management support via rpm / dnf
Further pruning is possible
  Custom distro configuration
  Set FORCE_RO_REMOVE to remove update-alternatives, etc. if not using package management

## Slide 140: Example distro configuration: schooner.conf
require conf/distro/poky.conf
DISTRO = "schooner"
DISTRO_NAME = "Schooner"
DISTRO_VERSION = "1.0-${DATE}"
DISTRO_CODENAME = "warrior"
SDK_VENDOR = "-schoonersdk"
MAINTAINER = "Scott Murray <scott.murray@konsulko.com>"
TARGET_VENDOR = "-schooner"
TCLIBC = "musl"
DISTRO_FEATURES = "acl ipv4 ipv6 largefile xattr virtualization"
VIRTUAL-RUNTIME_dev_manager ?= ""
VIRTUAL-RUNTIME_login_manager ?= ""
VIRTUAL-RUNTIME_init_manager ?= ""
VIRTUAL-RUNTIME_initscripts ?= ""
VIRTUAL-RUNTIME_keymaps ?= ""
PREFERRED_PROVIDER_virtual/kernel = "linux-dummy"

## Slide 141: Application Container Example

## Slide 142: Base application image: app-container-image.bb
SUMMARY = "A minimal container image"
LICENSE = "MIT"
LIC_FILES_CHKSUM = \
"file://${COREBASE}/meta/COPYING.MIT;md5=3da9cfbcb788c80a0384361b4de20420"
IMAGE_FSTYPES = "container"
inherit image
IMAGE_FEATURES = ""
IMAGE_LINGUAS = ""
NO_RECOMMENDATIONS = "1"
FORCE_RO_REMOVE = "1"
MACHINE_ESSENTIAL_EXTRA_RDEPENDS = ""
IMAGE_INSTALL = " \
base-files \
netbase \
"
# Workaround /var/volatile for now
ROOTFS_POSTPROCESS_COMMAND += "rootfs_fixup_var_volatile ; "
rootfs_fixup_var_volatile () {
install -m 1777 -d ${IMAGE_ROOTFS}/${localstatedir}/volatile/tmp
install -m 755 -d ${IMAGE_ROOTFS}/${localstatedir}/volatile/log
}

## Slide 143: app-container-image-lighttpd.bb
SUMMARY = "A lighttpd container image"
LICENSE = "MIT"
LIC_FILES_CHKSUM = \
"file://${COREBASE}/meta/COPYING.MIT;md5=3da9cfbcb788c80a0384361b4de20420"
require app-container-image.bb
# Note that busybox is required to satisfy /bin/sh requirement of lighttpd,
# and the access* modules need to be explicitly specified since RECOMMENDATIONS
# are disabled.
IMAGE_INSTALL += " \
busybox \
lighttpd \
lighttpd-module-access \
lighttpd-module-accesslog \
"

## Slide 144: Resulting image manifest
base-files qemux86_64 3.0.14
busybox core2_64 1.30.1
libattr1 core2_64 2.4.47
libcrypto1.1 core2_64 1.1.1b
libpcre1 core2_64 8.43
lighttpd core2_64 1.4.53
lighttpd-module-access core2_64 1.4.53
lighttpd-module-accesslog core2_64 1.4.53
lighttpd-module-dirlisting core2_64 1.4.53
lighttpd-module-indexfile core2_64 1.4.53
lighttpd-module-staticfile core2_64 1.4.53
musl core2_64 1.1.21+git0+43e7efb465
netbase core2_64 5.6

## Slide 145: Notes
bash may get pulled into images because of script detection during packaging
If the application expects to exec /bin/sh, busybox may need to be added manually as a dependency
The lack of post-install scripts means some tweaking may be required to e.g. create volatile directories
container-base.bb added to meta-virtualization in warrior based on app-container-image.bb, but specific to OCI container images

## Slide 146: Multiconfig

## Slide 147: Multiconfig
bitbake feature that allows building multiple images or packages for different targets where each image or package uses a different configuration
  multiple configurations -> multiconfigs
  https://www.yoctoproject.org/docs/2.7.1/dev-manual/dev-manual.html#dev-building-images-for-multiple-targets-using-multiple-configurations
Use cases?
  Potentially simplify builds of multiple images with minor differences
  Cross-build dependencies possible

## Slide 148: Multiconfig usage
Add MULTICONFIG variable definition to local.conf
Create "multiconfig" directory in "conf", and populate it with configuration file for each multiconfig listed in MULTICONFIG
Build with "bitbake multiconfig:<config>:<target>"
  Can use "mc:" in master / zeus
MULTICONFIG = "a b"
$ cat multiconfig/a.conf
MACHINE=qemux86-64
$ cat multiconfig/b.conf
MACHINE=qemux86
TMPDIR="${TOPDIR}/tmp-x86"

## Slide 149: Multiconfig notes
A lot of use cases will require separate TMPDIR settings for the multiconfigs
  Per documentation, configs with same MACHINE and TCLIBC are likely okay with same TMPDIR
At the moment there is no leveraging of the sstate-cache between multiconfigs (documentation calls this out)
An instance of bitbake is spawned for each multiconfig, plus one parent instance
Cross multiconfig dependencies are done with mcdepends
  task_or_package[mcdepends] = "multiconfig:<from>:<to>:<recipe>:<task>"
One multiconfig cannot use variables defined in another
  e.g. DEPLOY_DIR, variables set by DISTRO
  But can see global configuration variables from local.conf, etc.

## Slide 150: Containers and multiconfig?
So far we’ve been building container images on their own
Useful for “docker import” or similar on target, or “docker compose”, etc., then fetching over the network to target
What if we wanted to build a container image into a target image for a device?
  Building factory images for devices running application sandboxes
Somewhat constrained by tooling
  Currently only systemd-nspawn and runc seem straightforward
  Other systems might be supported by using post-install scripts to import container images, or perhaps via qemu

## Slide 151: Multiconfig Nested Container Example

## Slide 152: Multiconfig setup
local.conf
multiconfig/container.conf
CONTAINER_TMPDIR = "${TOPDIR}/tmp-container"
MACHINE = "qemux86-64"
DISTRO="marina"
MULTICONFIG = "container"
DISTRO = "schooner"
TMPDIR = "${CONTAINER_TMPDIR}"

## Slide 153: host-app-container-lighttpd.bb
SUMMARY = "Package lighttpd app container image"
LICENSE = "MIT"
LIC_FILES_CHKSUM = "file://${COREBASE}/meta/COPYING.MIT;md5=3da9cfbcb788c80a0384361b4de20420"
DEPENDS = "tar-native"
SRC_URI = "file://${CONTAINER_NAME}.nspawn"
do_compile[noexec] = "1"
do_install[mcdepends] = "multiconfig::container:${CONTAINER_NAME}:do_image_complete"
CONTAINER_NAME = "app-container-image-lighttpd"
CONTAINER_TMPDIR ?= "${TMPDIR}"
CONTAINER_MACHINE ?= "${MACHINE}"
CONTAINER_DEPLOY_DIR ?= "${CONTAINER_TMPDIR}/deploy/images/${CONTAINER_MACHINE}"
do_install () {
install -d ${D}/var/lib/machines/${CONTAINER_NAME}
tar -C ${D}/var/lib/machines/${CONTAINER_NAME} -xf \
${CONTAINER_DEPLOY_DIR}/${CONTAINER_NAME}-${CONTAINER_MACHINE}.tar.bz2
install -d ${D}${sysconfdir}/systemd/nspawn
install -m 0644 ${WORKDIR}/${CONTAINER_NAME}.nspawn ${D}${sysconfdir}/systemd/nspawn/
install -d ${D}${sysconfdir}/systemd/system/machines.target.wants
ln -sf ${systemd_system_unitdir}/systemd-nspawn@.service \
${D}${sysconfdir}/systemd/system/machines.target.wants/systemd-nspawn@${CONTAINER_NAME}.service
}
RDEPENDS_${PN} += "systemd-container"
INSANE_SKIP_${PN} += "build-deps dev-so already-stripped"

## Slide 154: marina.conf
require conf/distro/poky.conf
DISTRO = "marina"
DISTRO_NAME = "Marina"
DISTRO_VERSION = "1.0-${DATE}"
DISTRO_CODENAME = "master"
SDK_VENDOR = "-marinasdk"
MAINTAINER = "Scott Murray <scott.murray@konsulko.com>"
TARGET_VENDOR = "-marina"
DISTRO_FEATURES = "acl ipv4 ipv6 largefile xattr"
DISTRO_FEATURES_append = " systemd"
DISTRO_FEATURES_BACKFILL_CONSIDERED += "sysvinit"
VIRTUAL-RUNTIME_init_manager = "systemd"
VIRTUAL-RUNTIME_initscripts = ""

## Slide 155: app-container-image-lighttpd.nspawn
[Exec]
Boot=false
Parameters=/usr/sbin/lighttpd -D -f /etc/lighttpd/lighttpd.conf
LinkJournal=no
PrivateUsers=false
[Network]
VirtualEthernet=false

## Slide 156: container-host-image.bb
SUMMARY = "A minimal container host image" LICENSE = "MIT" LIC_FILES_CHKSUM = \
"file://${COREBASE}/meta/COPYING.MIT;md5=3da9cfbcb788c80a0384361b4de20420" require recipes-core/images/core-image-minimal.bb IMAGE_FEATURES += "ssh-server-openssh" IMAGE_INSTALL += " \ kernel-modules \ host-app-container-lighttpd \ "

## Slide 157: Outstanding issues
There's still a lot of room for improvement
  refactoring into a set of include files or classes
  tinkering with systemd-nspawn private networking and user namespace support
Final goal is to get OCI images working with runc
  runc will work without systemd
  systemd 242 in master also has OCI image support for systemd-nspawn
  Currently can build with some hacking, but issues getting OCI image runtime configuration generated to work on the host

## Slide 158: Resources
Jérémy Rosen presentation “Yoctoception: Containers in the embedded world”:
  https://www.slideshare.net/ennael/embedded-recipes-2018-yoctoception-containers-in-the-embedded-world-jrmy-rosen
  Simpler non-multiconfig nesting restricted to common MACHINE, DISTRO, TCLIBC configuration
Previous presentation at ELCE
  https://elinux.org/images/6/62/Building-Container-Images-with-OpenEmbedded-and-the-Yocto-Project-Scott-Murray-Konsulko-Group-1.pdf
  https://youtu.be/OSyLoHYxGLQ
Examples
  https://github.com/konsulko/meta-container-demo
  Will be updated with OCI image examples when I get it working

## Slide 159: Activity Seven
Devtool, next steps
Trevor Woerner
Presented by David Reyna

## Slide 160
devtool
a collection of tools for working on recipes
    devtool add
    devtool edit-recipe
    devtool upgrade
    devtool update-recipe
    etc...

## Slide 161
devtool
...and more!
    devtool modify
    devtool deploy-target
    devtool undeploy-target
    devtool build
    devtool build-image
    etc...

## Slide 162
devtool – past presentations
ELC 2017
    Using Devtool To Streamline Your Yocto Project Workflow - Tim Orling
    https://www.youtube.com/watch?v=CiD7rB35CRE
ELC 2017
    Yocto Project Extensible SDK: Simplifying the Workflow for Application Developers - Henry Bruce
    https://www.youtube.com/watch?v=d3xanDJuXRA&t=57s

## Slide 163
devtool – past presentations
ELC 2018
    Working with the Linux Kernel in the Yocto Project - Sean Hudson
    https://www.youtube.com/watch?v=tZACGS5nQxw

## Slide 164
devtool – past presentations
YPDD 2018 - ELC
    Session 3, Devtool 1 - Tim Orling
    https://www.youtube.com/watch?v=C-usM6gFVSY
YPDD 2018 - ELC
    Session 7, Devtool 2 - Tim Orling & Henry Bruce
    https://www.youtube.com/watch?v=UYsqIP_Qt_Q

## Slide 165
devtool – documentation
Yocto Project Reference Manual
    chapter 8 - devtool Quick Reference
    https://www.yoctoproject.org/docs/current/ref-manual/ref-manual.html#ref-devtool-reference
Yocto Project Application Development and the Extensible Software Development Kit (eSDK)
    chapter 2 - Using the Extensible SDK
    https://www.yoctoproject.org/docs/current/sdk-manual/sdk-manual.html#sdk-extensible

## Slide 166
devtool – documentation
Yocto Project Linux Kernel Development Manual
    section 2.4 - Using devtool to Patch the Kernel
    https://www.yoctoproject.org/docs/current/kernel-dev/kernel-dev.html#using-devtool-to-patch-the-kernel

## Slide 167
devtool – documentation
$ devtool --help
usage: devtool [--basepath BASEPATH] [--bbpath BBPATH] [-d] [-q]
[--color COLOR] [-h]
<subcommand> ...
OpenEmbedded development tool
options:
--basepath BASEPATH Base directory of SDK / build directory
--bbpath BBPATH Explicitly specify the BBPATH, rather than getting it
from the metadata
-d, --debug Enable debug output
-q, --quiet Print only errors
--color COLOR Colorize output (where COLOR is auto, always, never)
-h, --help show this help message and exit
subcommands:
Beginning work on a recipe:
add Add a new recipe
...

## Slide 168
devtool – documentation
$ devtool add --help
usage: devtool add [-h] [--same-dir | --no-same-dir] [--fetch URI]
[--fetch-dev] [--version VERSION] [--no-git]
[--srcrev SRCREV | --autorev] [--srcbranch SRCBRANCH]
[--binary] [--also-native] [--src-subdir SUBDIR]
[--mirrors] [--provides PROVIDES]
[recipename] [srctree] [fetchuri]
Adds a new recipe to the workspace to build a specified source tree. Can
optionally fetch a remote URI and unpack it to create the source tree.
arguments:
recipename Name for new recipe to add (just name - no version,
path or extension). If not specified, will attempt to
auto-detect it.
srctree Path to external source tree. If not specified, a
subdirectory of /z/ypdd/2018-10-devtool/my-
class/poky/build/workspace/sources will be used.
fetchuri Fetch the specified URI and extract it to create the
source tree
options:
-h, --help show this help message and exit
...

## Slide 169
devtool development – contributors – by commits
* as of Oct 15, 2018
Chart: 
| Paul Eggleton | Markus Lehtonen | Ed Bartosh | Richard Purdie | Leonardo Sandoval | Ola x Nilsson | Alexander Kanavin | Randy Witt | Chen Qi | Chang Rebecca Swee Fun | Stephano Cetola | Christopher Larson | Tzu-Jung Lee | Peter Kjellerstedt | Joshua Lock | Daniel Lublin | Tobias Hagelborn | Tim Orling | Saul Wold | Ming Liu | Luck Hoang | Khem Raj | Juro Bystricky | Junchun Guan | Juan M Cruz Alcaraz | Joe MacDonald | Jiajie Hu | brian avery | Brendan Le Foll | Aníbal Limón | Andrea Galbusera | Anders Darander
Column B | 250 | 43 | 21 | 11 | 6 | 5 | 5 | 4 | 5 | 4 | 3 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 170
devtool development – contributors – by lines
* as of Oct 15, 2018
Chart: 
| Paul Eggleton | Leonardo Sandoval | Markus Lehtonen | Qi.Chen windriver.com | Alexander Kanavin | Ed Bartosh | Tzu-Jung Lee | Joshua Lock | Junchun Guan | Brendan Le Foll | Juan M Cruz Alcaraz | Randy Witt | Christopher Larson | Chang Rebecca Swee Fun | Tobias Hagelborn | Richard Purdie | Tim Orling | Daniel Lublin | Ola x Nilsson | Saul Wold | Ming Liu | Luck Hoang | Jiajie Hu | brian avery | Anders Darander | Peter Kjellerstedt | Stephano Cetola | Khem Raj | Joe MacDonald | Andrea Galbusera
Column B | 3596 | 549 | 424 | 125 | 121 | 66 | 57 | 56 | 47 | 43 | 41 | 31 | 30 | 30 | 25 | 18 | 14 | 6 | 5 | 4 | 4 | 4 | 3 | 3 | 3 | 2 | 1 | 1 | 1 | 1

## Slide 171
devtool development - functionality

## Slide 172
devtool development – commits
Chart: commits
| 1.8 fido | 2.0 jethro | 2.1 krogoth | 2.2 morty | 2.3 pyro | 2.4 rocko | 2.5 sumo | master
Column C | 35 | 105 | 100 | 39 | 35 | 33 | 33 | 4

## Slide 173
devtool – modes
devtool runs in two modes
    when run inside an eSDK: “eSDK mode”
    when run outside an eSDK: “bitbake mode”

## Slide 174
devtool – mode commands
bitbake mode
    add
    build
    build-image
    configure-help
    create-workspace
    deploy-target
    edit-recipe
    export
    extract
    find-recipe
    finish
    import
    latest-version
    modify
    rename
    reset
    search
    status
    sync
    undeploy-target
    update-recipe
    upgrade
eSDK mode
    add
    build
    build-image
    build-sdk
    configure-help
    deploy-target
    edit-recipe
    export
    extract
    find-recipe
    finish
    import
    latest-version
    modify
    package
    rename
    reset
    runqemu
    sdk-install
    sdk-update
    search
    status
    sync
    undeploy-target
    update-recipe
    upgrade

## Slide 175
devtool – mode commands
why does eSDK mode get all the extra features?
    because an eSDK doesn’t have bitbake or scripts/
    devtool is the cornerstone of the eSDK

## Slide 176
devtool – workspace
a separate environment (layer) in which to work on recipes, sources, patches

## Slide 177
devtool – workspace (bitbake mode)
how the various devtool commands relate to the your layers, your target, and your workspace
add
modify
upgrade
finish
reset
deploy-target
undeploy-target
build
rename
find-recipe search edit-recipe latest-version
configure-help
status
build-image
update-recipe

## Slide 178
devtool – multiple targets?

## Slide 179
devtool – multiple targets?
yes
specify target’s IP with un/deploy-target

## Slide 180
devtool – multiple workspaces?

## Slide 181
devtool – multiple workspaces?
technically: yes (i.e. no errors)
practically: no (the next replaces the previous, so there’s only ever one)

## Slide 182
devtool – setup
$ edit/create ~/.ssh/config
$ cd ~/scratch
$ git clone -b warrior git://git.yoctoproject.org/poky
$ . poky/oe-init-build-env build
$ edit conf/local.conf
MACHINE = "qemuarm"
DL_DIR = "/scratch/downloads"
SSTATE_DIR = "/scratch/sstate-cache"
INHERT += "buildhistory"
IMAGE_INSTALL_append = " openssh"
WARN_QA_append = " version-going-backwards"
ERROR_QA_remove = "version-going-backwards"
Host qemu
User root
Hostname localhost
Port 2222
StrictHostKeyChecking no
UserKnownHostsFile /dev/null

## Slide 183
devtool – setup
$ bitbake core-image-base
$ bitbake-layers create-layer ../meta-foo
$ bitbake-layers add-layer ../meta-foo
$ git config --global user.name "name"
$ git config --global user.email "name@server.com"
open a second ssh connection to the build machine
do the exercises in the first connection, work on the target in the second connection
$ cd ~/scratch/poky
$ . oe-init-build-env build
$ runqemu slirp nographic serial

## Slide 184
devtool – getting started
$ devtool add \
https://nano-editor.org/dist/v3/nano-3.0.tar.xz
implicitly creates workspace (if it doesn’t already exist)
guesses the recipe name “nano” (correctly!)
looks at the source and determines it’s an autotooled project (true! and pkgconfig and gettext)
guesses at DEPENDS (correctly!)
creates a “rough” recipe
$ devtool status
$ devtool find-recipe nano
$ devtool edit-recipe nano

## Slide 185
devtool – getting started
let’s see if it builds
it works!
$ devtool build nano

## Slide 186
devtool – what goes in a workspace?
the things on which you are working:
    recipes
    patches
    sources
    etc...
...except sources can be, optionally, outside the workspace
$ tree -d workspace

## Slide 187
devtool – let’s see nano run
examine buildhistory/images/qemuarm/glibc/core-image-base/installed-packages.txt
    verify there’s no “nano” package
in the terminal running qemu, log in and verify there’s no nano
send nano to target
now nano runs
root@qemuarm# nano
-sh: nano: command not found
$ devtool deploy-target nano qemu

## Slide 188
build an entire image
examine buildhistory/......./installed-packages.txt
    now there is a “nano” package
why not just use “bitbake core-image-base”?
    nano package not automatically added
    devtool makes assumptions
devtool – let’s see nano run
$ devtool build-image core-image-base
...
NOTE: Building image core-image-base with the following additional packages: nano
...
Notes: build-image = 2 minutes

## Slide 189
devtool – upgrade
$ devtool upgrade -V 3.1 nano
ERROR: recipe nano is already in your workspace
try upgrading nano
$ devtool finish nano ../meta-foo
ERROR: Source tree is not clean:
...
we need to move recipe to layers before upgrade
    preferably our own (meta-foo)
this is not a problem we introduced
$ devtool finish -f nano ../meta-foo

## Slide 190
devtool – upgrade
$ devtool upgrade -V 3.1 nano
$ devtool build nano
$ devtool deploy-target nano qemu

## Slide 191
devtool deploy-target - dive in
is it okay to re-deploy a second time without cleaning up the first deploy?
    yes... usually
on the target
root@qemuarm# cd /
root@qemuarm# ls -a
...
.devtool
...
root@qemuarm# cd .devtool
root@qemuarm# ls -l
-rw-r--r-- 1 root root 4969 Oct 20 06:03 nano.list

## Slide 192
devtool deploy-target - dive in
nano.list is created by devtool, per package, when it deploys to the target
examine poky/scripts/lib/devtool/deploy.py for all the answers
    it creates a script that is copied to target
    preserves any files that would be clobbered
    generates a list of files being deployed, so they can be undeployed
    deploying starts by undeploying (same recipe name)

## Slide 193
devtool deploy-target - dive in
undeploy, and verify nano is removed from target, and the plumbing is also removed
$ devtool undeploy-target nano qemu
root@qemuarm# ls -a /
$ devtool finish -f nano ../meta-foo
$ rm -fr workspace/sources/nano
remember to finish and cleanup

## Slide 194
devtool - floating devtool commands
some devtool commands don’t care whether the recipe is in the workspace or the layers
$ devtool status
NOTE: No recipes currently in your workspace
$ devtool edit-recipe bash
(works)
$ devtool latest-version bash
NOTE: Current version: 4.4.18
NOTE: Latest version: 5.0
$ devtool find-recipe bash
$ devtool search bash

## Slide 195
devtool - multiple workspaces
let’s look at some devtool plumbing
$ cat conf/devtool.conf
[General]
workspace_path = /scratch/poky/build/workspace
[SDK]
target_basename = core-image-base
$ tail -3 conf/bblayers.conf
/scratch/poky/meta-foo \
/scratch/poky/build/workspace \
"

## Slide 196
devtool - multiple workspaces
create a new workspace
$ devtool create-workspace ws2
$ head -2 conf/devtool.conf
[General]
workspace_path = /home/ilab01/devtool/build/ws2
$ tail -3 conf/bblayers.conf
/home/ilab01/devtool/meta-foo \
/home/ilab01/devtool/build/ws2 \
"
the first one disappears

## Slide 197
devtool - creating a patch
use-case? patches can be needed to
    add/remove functionality
        reduce size
        remove dependency/dependencies
    allow code to be (cross-)compiled

## Slide 198
devtool - creating a patch
$ devtool add https://github.com/twoerner/ypdd-elce2018-example/archive/v1.0.0.tar.gz
$ devtool build ypdd-elce2018-example
$ devtool deploy-target ypdd-elce2018-example qemu
root@qemuarm# ypdd-elce2018-example
Hello, world!
Hello from the library

## Slide 199
devtool - creating a patch
edit the code
$ export EDITOR=vi
$ pushd workspace/sources/ypdd-elce2018-example
$ $EDITOR src/ypdd-elce2018-example.c
change from
printf("Hello, world!\n");
to
printf("Hello, San Diego!\n");

## Slide 200
devtool - creating a patch
build, deploy, verify
$ popd
$ devtool build ypdd-elce2018-example
$ devtool deploy-target ypdd-elce2018-example qemu
root@qemuarm# ypdd-elce2018-example
Hello, Edinburgh!
Hello from the library

## Slide 201
devtool - creating a patch
cleanup
$ devtool finish ypdd-elce2018-example ../meta-foo
ERROR: Source tree is not clean:
M src/ypdd-elce2018-example.c
oops! but it’s nice it didn’t clobber or lose my work
$ pushd workspace/sources/ypdd-elce2018-example
$ git commit -avs
...
$ popd
$ devtool finish ypdd-elce2018-example ../meta-foo
...
NOTE: Adding new patch 0001-update-salutation.patch
...
$ rm -fr workspace/sources/ypdd-elce2018-example

## Slide 202
devtool - creating conflict
now we’ll update to a newer release, but the newer release will conflict with our patch
$ devtool upgrade ypdd-elce2018-example
...
--2018-10-20 12:16:11-- https://github.com/twoerner/ypdd-elce2018-example/archive/
Resolving github.com (github.com)... 192.30.253.113, 192.30.253.112
Connecting to github.com (github.com)|192.30.253.113|:443... connected.
HTTP request sent, awaiting response... 404 Not Found
2018-10-20 12:16:11 ERROR 404: Not Found.
NOTE: Current version: 1.0.0
NOTE: Latest version:
devtool can’t figure it out, we need to help it

## Slide 203
devtool - creating conflict
$ devtool upgrade -V 1.0.1 ypdd-elce2018-example
...
WARNING: Command 'git rebase 99271b82b92d8f5f9ecb31099b78895ba7da84ef' failed:
First, rewinding head to replay your work on top of it...
Applying: update salutation
Using index info to reconstruct a base tree...
M src/ypdd-elce2018-example.c
Falling back to patching base and 3-way merge...
Auto-merging src/ypdd-elce2018-example.c
CONFLICT (content): Merge conflict in src/ypdd-elce2018-example.c
error: Failed to merge in the changes.
Patch failed at 0001 update salutation
The copy of the patch that failed is found in: .git/rebase-apply/patch
When you have resolved this problem, run "git rebase --continue".
If you prefer to skip this patch, run "git rebase --skip" instead.
To check out the original branch and stop rebasing, run "git rebase --abort".
You will need to resolve conflicts in order to complete the upgrade.

## Slide 204
devtool - relieving conflict
keep the new, or keep the old?
    keep the new
$ pushd workspace/sources/ypdd-elce2018-example
$ $EDITOR src/ypdd-elce2018-example.c

## Slide 205
devtool - relieving conflict
from
12 <<<<<<< 99271b82b92d8f5f9ecb31099b78895ba7da84ef
13 /* a meaningful comment */
14 printf("Hello, world!\n");
15 =======
16 printf("Hello, San Diego!\n");
17 >>>>>>> update salutation
to
12 /* a meaningful comment */
13 printf("Hello, San Diego!\n");

## Slide 206
devtool - relieving conflict
$ git add src/ypdd-elce2018-example.c
$ git rebase --continue
Applying: update salutation
$ popd
$ devtool update-recipe ypdd-elce2018-example
inspect recipe updates

## Slide 207
devtool - relieving conflict
$ devtool finish ypdd-elce2018-example ../meta-foo
$ tree ../meta-foo
../meta-foo/
...
├── recipes-nano
│ └── nano
│ └── nano_3.1.bb
└── recipes-ypdd-elce2018-example
└── ypdd-elce2018-example
├── ypdd-elce2018-example
│ └── 0001-update-salutation.patch
└── ypdd-elce2018-example_1.0.1.bb
considering there’s devtool finish, how useful is devtool update-recipe?

## Slide 208
devtool - modify
take existing recipe from layers
move recipe to workspace
unpack sources into workspace
edit recipe or sources

## Slide 209
devtool - eSDK Mode
the eSDK includes many improvements over the SDK
combine everything of a regular SDK with all the functionality we’ve been looking at that is provided by devtool

## Slide 210
Questions

## Slide 211: Activity Eight
Tools, Toaster, User Experience
David Reyna

## Slide 212: Toaster: Latest Features (1/2)
Toaster Documentation
  https://www.yoctoproject.org/docs/latest/toaster-manual/toaster-manual.html
Toaster Service Without a Web Server (“noweb”)
  Good for capturing command line build(s) directly into the db
Toaster Service Without Remote Builds (“nobuild”)
  Good for sharing build local status, without enabling external people creating projects and starting builds on your host
Toaster Service – Build Status within Containers
  New REST/JSON API to access the progress and health of bitbake builds via HTTP; very handy for containers
  Build Status options: “Completed”, “In Progress”, “Specific Status”

## Slide 213: Toaster: Latest Features (2/2)
Compatibility between Command Line and Toaster builds
  New “Import command line build” option
  New “Merge Toaster Settings” into standard conf files”

## Slide 214: Intel System Studio 2019: Yocto Project Compatible
The Wind River Application and Project plug-ins have been shared with Intel System Studio, with the idea of open sourcing them to Eclipse.org
Implementation is architecture agnostic
Application Project Features:
  Awareness of YP compatible SDKs/eSDKs
  Ability to register multiple SDKs
  Automatic generation of “Build Specs” for each machine variant in each SDK
  Ability to enable/disable debug flags
  Debugger deploy and access over GDB/TCF
  Set of sample applications

## Slide 215: Intel System Studio 2019: Yocto Project Compatible
Platform Project Features:
  Configuration/Updates via Toaster
  Basic build targets directly from ISS
  Eclipse-based Kernel Configuration Tool
  Tree view to browse deploy artifacts

## Slide 216: Intel System Studio 2019: Yocto Project Compatible
Import:
  Existing command line project
  Existing SDK/eSDK

## Slide 217: New Security Response Tool (SRTool)
While there is heighten awareness about device vulnerabilities, what is often missing is awareness about the process of managing the security response process itself
Wind River is sharing to open source a tool to help manager the organization’s security response management:
  Better ways to handle 1000+ CVEs per month
  Better ways to connect CVE’s to defects to product
  Better ways to allow easy access to the full vulnerability status, generate reports, clean exports to public CVE DB
  Better ways to use automation to keep all the data sources automatically up to date
Community Page:
  https://wiki.yoctoproject.org/wiki/Contribute_to_SRTool
ELCE Presentation:
  https://sched.co/HOLr

## Slide 218: Questions and Answers

## Slide 219: Thank you for your participation!

## Slide 220: Activity Bonus #1
Yocto Project - Rarely asked questions
Khem Raj

## Slide 221: How to add layers to Workspace
bitbake-layers
  add-layer/remove-layer – Add/Remove a layer to workspace
  show-layer – Show current list of used layers
  show-recipes – List available recipes
  show-appends – List appends and corresponding recipe
  show-overlayed – List overlayed recipes

## Slide 222: Are there some Workspace helper Tools
bitbake-whatchanged
  print what will be done between the current and last builds
        $ bitbake core-image-sato
        # Edit the recipes
        $ bitbake-whatchanged core-image-sato

## Slide 223: How to make changes in workspace
Prepare a package to make changes
          devtool modify <recipe>
Change sources
  Change into workspace/sources/<recipe>
  Edit …..
Build Changes
        devtool build <recipe>
Test changes
        devtool deploy-target <recipe> <target-IP>
Make changes final
        devtool finish <recipe> <layer>

## Slide 224: How to enquire package information ?
oe-pkgdata-util - queries the pkgdata files written out during do_package
        subcommands:
        lookup-pkg Translate between recipe-space package names and
        runtime package names
        list-pkgs List packages
        list-pkg-files List files within a package
        lookup-recipe Find recipe producing one or more packages
        package-info Show version, recipe and size information for one or
        more packages
        find-path Find package providing a target path
        read-value Read any pkgdata value for one or more packages
        glob Expand package name glob expression
        Use oe-pkgdata-util <subcommand> --help to get help on a specific command

## Slide 225: How to run meta-data self tests (unit tests)
oe-selftest
          Script that runs unit tests against bitbake and other Yocto related tools. The goal is to validate tools functionality and metadata integrity
  List available tests
        oe-selftest –l
  Run all tests
        oe-selftest --run-all-tests
  Run Selective Unit Test
        oe-selftest -r devtool devtool.DevtoolTests.test_devtool_add_fetch_simple
https://wiki.yoctoproject.org/wiki/Oe-selftest
Notes: -–run-tests-by <name|class|module|id|tag>
Name
--run-tests-by name testA testB testC: simply specify test names and it will determine automatically where they are located.
class--run-tests-by class classA classB classC: simply specify class names and it will determine automatically what tests they contain and where they are located.

## Slide 226: How to run image auto-test
Can test image ( -c testimage) (-c testimage_auto)
Testing SDK ( -c testsdk and –c testsdkext)
https://www.yoctoproject.org/docs/latest/dev-manual/dev-manual.html#performing-automated-runtime-testing
INHERIT += "testimage"
DISTRO_FEATURES_append = " ptest"
EXTRA_IMAGE_FEATURES_append = " ptest-pkgs"
##TEST_SUITES = "auto"
TEST_IMAGE_qemuall = "1"
TEST_TARGET_qemuall = "qemu”
TEST_TARGET ?= "simpleremote"
TEST_SERVER_IP = "10.0.0.10"
TEST_TARGET_IP ?= "192.168.7.2"
INHERIT += "testsdk"
SDK_EXT_TYPE = "minimal"
Notes: Type of tests
Runtime
SDK
SDK-EXT
Self-test

## Slide 227: How to send Code upstream
create-pull-request
        Examples:
        create-pull-request -u contrib -b joe/topic
send-pull-request
        Examples:
          Send-pull-request –a –p pull-XXXX

## Slide 228: How to Customize Distro
Example poky-lsb
          require conf/distro/poky.conf
          require conf/distro/include/security_flags.inc
          DISTRO = "poky-lsb"
          DISTROOVERRIDES = "poky:linuxstdbase"
          DISTRO_FEATURES_append = " pam largefile opengl"
          PREFERRED_PROVIDER_virtual/libx11 = "libx11"
          # Ensure the kernel nfs server is enabled
          KERNEL_FEATURES_append_pn-linux-yocto = " features/nfsd/nfsd-enable.scc"
          # Use the LTSI Kernel for LSB Testing
          PREFERRED_VERSION_linux-yocto_linuxstdbase ?= "4.14%"

## Slide 229: How to Customize Machine
odroid-c2-hardkernel.conf
          #@TYPE: Machine
          #@NAME: odroid-c2-hardkernel
          #@DESCRIPTION: Machine configuration for odroid-c2 systems using uboot/kernel from hardkernel supported vendor tree
          #@MAINTAINER: Armin Kuster <akuster808@gmail.com>
          require conf/machine/odroid-c2.conf
          SERIAL_CONSOLE = "115200 ttyS0"
          UBOOT_CONSOLE = "console=ttyS0,115200"
          KERNEL_DEVICETREE_FN_odroid-c2-hardkernel = "meson64_odroidc2.dtb"
          KERNEL_DEVICETREE_odroid-c2-hardkernel = "meson64_odroidc2.dtb"
odroid-c2.conf
          #@TYPE: Machine
          #@NAME: odroid-c2
          #@DESCRIPTION: Machine configuration for odroid-c2 systems
          #@MAINTAINER: Armin Kuster <akuster808@gmail.com>
          require conf/machine/include/amlogic-meson64.inc
          DEFAULTTUNE ?= "aarch64"
          include conf/machine/include/odroid-default-settings.inc
          EXTRA_IMAGEDEPENDS += "u-boot secure-odroid"
          KERNEL_DEVICETREE_FN = "meson-gxbb-odroidc2.dtb"
          KERNEL_DEVICETREE = "amlogic/meson-gxbb-odroidc2.dtb"

## Slide 230: How to setup/use feeds ?
Configuring feeds in image
        PACKAGE_FEED_URIS = "http://10.0.0.10:8000/"
Start a http server in deploydir
        cd tmp/deploy/ipk
        python3 -m http.server 8000
Run Package manager on booted target
        opkg update
        opkg upgrade

## Slide 231: Activity Bonux #2
A User's Experience
Henry Bruce

## Slide 232: What I’ll be talking about
Learnings from my painful ramp on Yocto
Get similar experiences from the audience
Funnel these learnings into topics in the new Development Tasks Manual
Review improvements in usability over the past few years

## Slide 233: General areas I’ll be covering
Proxies
Debugging build errors
Writing recipes
Recipes vs. Packages
Application Development
Cool things I stumbled across
Improvements

## Slide 234: Some context
Started as an open source neophyte
  Had never really used git or dug into Linux
Spent six months in extreme pain
  Mainly due to OpenJDK
For the next year I was learning
After 2 years I felt I could competently help others
Over 3 years later, there's still so much to learn
I should have taken better notes

## Slide 235: Proxies
A common problem for new users
Proxy wiki page has 135k hits
  https://wiki.yoctoproject.org/wiki/Working_Behind_a_Network_Proxy
Environment variable approach covers most cases
  But fails when non-fetch tasks reach out to network
  This includes most node.js recipes
  How important is network isolation for post fetch tasks?
Chameleonsocks has been failsafe for me
  But some say this an abuse of docker
What’s your solution?

## Slide 236: When things go wrong
You’ve gone through the quick start guide and have figured out how to add packages to an image
You’re feeling pretty good but then you get a build error.
Due to many moving parts it’s easy to panic when something breaks
  Or at least it was for me

## Slide 237: It broke – what would have helped?
Nicer output from bitbake on bad directory/file names
Understanding the task pipeline
  fetch / unpack / configure / build / install / package
Knowing how to generate dependency graph
Decoding “magic” folder names in tmp/work
Understanding recipe vs. package
Knowing how to run specific task for specific recipe
Knowing what’s packaged and in rootfs

## Slide 238: Recipes
Plenty of resources to writing simple recipes
  But then there seems to be a gap
Can be hard to work out what a recipe is doing
pn = d.getVar('PN', 1)
metapkg = pn + '-dev'
d.setVar('ALLOW_EMPTY_' + metapkg, "1")
blacklist = [ metapkg ]
metapkg_rdepends = [ ]
packages = d.getVar('PACKAGES', 1).split()
for pkg in packages[1:]:
if not pkg in blacklist and pkg.endswith('-dev'):
metapkg_rdepends.append(pkg)
d.setVar('RRECOMMENDS_' + metapkg, ' '.join(metapkg_rdepends))
Walk through a couple of good citizens in oe-core?

## Slide 239: Recipes and packages
Easy to assume there is 1:1 mapping
Sometimes there isn’t
  devtool search rocks
Sub-packages can trip you up
  OpenCV vs. UPM
Creating sub-packages for large project seems to be the “right” pattern
  But I can’t find obvious guidance in docs
Thoughts?

## Slide 240: Application Development
I was initially confused by the terminology
  ADT, SDK, eSDK, toolchain
In retrospect ADT seemed the clearest naming
  I’m now working on a real-time SDK
  Yocto built Linux is our initial target platform
  I tell my team to develop for the target using the Yocto SDK
  Confusion all round
Eclipse
  Broken when I first tried
  I need to get back to it

## Slide 241: Improvements
eSDK and devtool
Recipetool
  ROS support
  Is it worth investing more, or do returns diminish?
Package feeds
  Credit to dnf (setting server means build checks if it’s there)
  But package-index is a big gotcha
Development Tasks Manual
CROPS
  Who’s using it?

## Slide 242: Cool things I stumbled across
PACKAGECONFIG
INSANE_SKIP
Overrides
Layer dependencies
Setting package variables from outside recipe
Conditional logic with python
  Adding package to image if its layer is present
What’s you favorite?

## Slide 243: Activity Bonus #3
U-Boot bootloader
Marek Vasut

## Slide 244
Booting contemporary hardware
Contemporary embedded system boots like this
  Power on
  (optional) BootROM
  (optional) First stage bootloader
  Next stage bootloader
  (optional) other bootloader stages
  Linux kernel
  Userspace
We will focus on the bootloader parts

## Slide 245
U-Boot bootloader
De-facto standard bootloader in embedded
  Capable of starting Linux, *BSD, RTOSes, UEFI apps
U-Boot is also a boot monitor
  U-Boot has a powerful command shell
  Allows manipulating with the boot process
    (boot different kernel, script the boot process...)
U-Boot is also a debug multitool
  U-Boot shell tools allow operating hardware blocks
    (memory IO, SPI, I2C, network, USB, ...)

## Slide 246
Experimenting with U-Boot bootloader
Three ways of doing that:
  U-Boot sandbox target
    U-Boot built as a Linux userspace binary
  QEMU
    U-Boot running in QEMU
  Real hardware (danger zone)
    U-Boot running on real HW
    Flashing incorrect bootloader brick the device :-)

## Slide 247
Experimenting with U-Boot bootloader in OE
Use the meta-dto-microdemo layer
Metalayer contains convenience recipes
  The u-boot-sandbox recipe
    To quickly build U-Boot sandbox native target
    See recipes-bsp/u-boot/
  Kernel config changes to enable virt platform
    See recipes-kernel/linux/files/force-virt.cfg
  DTO related things for later

## Slide 248
DTO Hands-on 1/2
Add meta-dto-demo to bblayers.conf BBLAYERS:
Rebuild u-boot, u-boot-sandbox-native and qemu-native
$ echo "BBLAYERS += \"/scratch/src/dto/meta-dto-microdemo\"" \
>> conf/bblayers.conf
$ echo "MACHINE = \"qemuarm\"" >> conf/local.conf
$ echo "SSTATE_DIR = \"/scratch/sstate-cache\"" >> conf/local.conf
$ echo "DL_DIR = \"/scratch/downloads\"" >> conf/local.conf
$ echo "UBOOT_MACHINE = \"qemu_arm_defconfig\"" >> conf/local.conf
$ bitbake -c cleansstate u-boot u-boot-sandbox-native qemu-native \
virtual/kernel
$ bitbake u-boot u-boot-sandbox-native u-boot-mkimage-native \
qemu-native virtual/kernel
Experimenting with U-Boot bootloader in OE
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
248

## Slide 249
DTO Hands-on 1/2
Start the u-boot sandbox (use Ctrl-C to exit)
$ ./tmp/work/x86_64-linux/u-boot-sandbox-native/\
1_2018.01-r0/git/u-boot
U-Boot 2018.01-dirty (Oct 14 2018 - 11:30:36 +0000)
[…]
SCSI: Net: No ethernet found.
IDE: Bus 0: not available
Hit any key to stop autoboot: 0
=>
=> help
? - alias for 'help'
base - print or set address offset
bootz - boot Linux zImage image from memory
[…]
=> help bootz
bootz - boot Linux zImage image from memory
Usage:
bootz [addr [initrd[:size]] [fdt]]
- boot Linux zImage stored in memory
The argument 'initrd' is optional and specifies the address
Experimenting with U-Boot bootloader in OE
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
249

## Slide 250
DTO Hands-on 1/2
Start U-Boot in QEMU
(CTRL-A x to quit QEMU)
$ ./tmp/work/x86_64-linux/qemu-native/\
2.11.1-r0/build/arm-softmmu/qemu-system-arm \
-machine virt \
-bios tmp/deploy/images/qemuarm/u-boot.bin -nographic
U-Boot 2018.01 (Oct 11 2018 - 13:14:21 +0000)
DRAM: 128 MiB
WARNING: Caches not enabled
Using default environment
In: pl011@9000000
Out: pl011@9000000
Err: pl011@9000000
Net: No ethernet found.
Hit any key to stop autoboot: 0
=>
Experimenting with U-Boot bootloader in OE
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
250

## Slide 251
DTO Hands-on 1/2
Generate suitable NOR flash image
Start U-Boot with this NOR flash image
$ dd if=/dev/zero of=/tmp/test.bin bs=16M count=0 seek=1
$ dd if=tmp/deploy/images/qemuarm/u-boot.bin \
of=/tmp/test.bin conv=notrunc
$ dd if=tmp/deploy/images/qemuarm/zImage \
of=/tmp/test.bin bs=1M seek=1 conv=notrunc
$ ./tmp/work/x86_64-linux/qemu-native/2.11.1-r0/\
build/arm-softmmu/qemu-system-arm \
-machine virt -bios /tmp/test.bin -nographic
U-Boot 2018.01 (Oct 11 2018 - 13:14:21 +0000)
DRAM: 128 MiB
In: pl011@9000000
Out: pl011@9000000
Err: pl011@9000000
Net: No ethernet found.
Hit any key to stop autoboot: 0
=>
Booting the kernel zImage
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
251

## Slide 252
DTO Hands-on 1/2
Figure out where the RAM is
Kernel is ~ 8 MiB, copy it to RAM start + 0x8000
=> cp 0x100000 0x40008000 0x200000
=> bdi
arch_number = 0x00000000
boot_params = 0x00000000
DRAM bank = 0x00000000
-> start = 0x40000000
-> size = 0x08000000
baudrate = 115200 bps
TLB addr = 0x47FF0000
relocaddr = 0x47F88000
reloc off = 0x47F88000
irq_sp = 0x46F66ED0
sp start = 0x46F66EC0
Early malloc usage: 104 / 400
fdt_blob = 46f66ee8
Booting the kernel zImage
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
252

## Slide 253
DTO Hands-on 1/2
Boot the zImage with DT
The $fdtcontroladdr is DT generated by QEMU
  You can dump the DT by appending -machine dumpdtb=file.dtb
=> bootz 0x40008000 - $fdtcontroladdr
Kernel image @ 0x40008000 [ 0x000000 - 0x524da0 ]
## Flattened Device Tree blob at 46f66ee8
Booting using the fdt blob at 0x46f66ee8
Using Device Tree in place at 46f66ee8, end 46f79ee7
Starting kernel ...
[ 0.000000] Booting Linux on physical CPU 0x0
[ 0.000000] Linux version 4.14.67-yocto-standard (oe-user@oe-host)
(gcc version 7.3.0 (GCC)) #1 PREEMPT Thu Oct 11 13:10:58 UTC 2018
[ 0.000000] CPU: ARMv7 Processor [412fc0f1] revision 1 (ARMv7), cr=10c53c7d
[ 0.000000] CPU: div instructions available: patching division code
[ 0.000000] CPU: PIPT / VIPT nonaliasing data cache, PIPT instruction cache
[ 0.000000] OF: fdt: Machine model: linux,dummy-virt
[ 0.000000] Memory policy: Data cache writeback
[ 0.000000] psci: probing for conduit method from DT.
[ 0.000000] psci: PSCIv0.2 detected in firmware.
Booting the kernel zImage
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
253

## Slide 254
Kernel image types – zImage and Image
zImage and Image
  Linux binary with decompressor
  No protection against bitrot
  Set up registers as needed and jump to it
  DT is optional and separate
  Boot with U-Boot “bootz” command
  On Aarch64, similar type of image is called Image
    Boot with “booti” command
uImage
fitImage

## Slide 255
Kernel image types – uImage
zImage and Image
uImage
  Envelope around arbitrary file
  Legacy since forever
  Small header with CRC32 and metadata
    Note that CRC32 is weak
    Metadata contain payload type, load address...
  Wraps only one single file
  Boot with “bootm” command
fitImage

## Slide 256
Kernel image types – fitImage
zImage and Image
uImage
FitImage
  Multi-component image
  Based on DT
  Can bundle multiple files with different properties
  Configurable checksum per-entry
    CRC32, MD5, SHA1, SHA256...
  Supports digital signatures
    RSA2048, RSA4096...

## Slide 257
DTO Hands-on 1/2
QEMU specific step – dump the DTB
Copy over the fitImage source from the metalayer
Build the fitImage:
=> $ qemu-system-arm -machine virt -nographic -machine dumpdtb=qemu.dtb
Building the kernel fitImage
$ cp /scratch/src/dto/meta-dto-microdemo/recipes-kernel/\
linux/files/fit-image.its .
$ export PATH=$PATH:tmp/work/x86_64-linux/dtc-native/\
1.4.5-r0/image/scratch/poky/build/tmp/work/x86_64-linux/\
dtc-native/1.4.5-r0/recipe-sysroot-native/usr/bin/
$ ./tmp/work/x86_64-linux/u-boot-mkimage-native/\
1_2018.01-r0/git/tools/mkimage -f ./fit-image.its /tmp/fitImage
FIT description: Linux kernel and FDT blob
Created: Sun Oct 14 12:57:59 2018
Image 0 (kernel-1)
Description: Linux kernel
Created: Sun Oct 14 12:57:59 2018
Type: Kernel Image
Compression: uncompressed
Data Size: 5393824 Bytes = 5267.41 KiB = 5.14 MiB
Architecture: ARM
OS: Linux
[…]
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
257

## Slide 258
DTO Hands-on 1/2
Generate suitable NOR flash image
Start U-Boot with this NOR flash image
$ dd if=/dev/zero of=/tmp/test.bin bs=16M count=0 seek=1
$ dd if=tmp/deploy/images/qemuarm/u-boot.bin \
of=/tmp/test.bin conv=notrunc
$ dd if=/tmp/fitImage \
of=/tmp/test.bin bs=1M seek=1 conv=notrunc
$ ./tmp/work/x86_64-linux/qemu-native/2.11.1-r0/\
build/arm-softmmu/qemu-system-arm \
-machine virt -bios /tmp/test.bin -nographic
[…]
=> setenv fdt_high 0x48000000
=> bootm 0x100000
## Loading kernel from FIT Image at 00100000 ...
Using 'conf-1' configuration
Trying 'kernel-1' kernel subimage
[…]
Loading Device Tree to 46f49000, end 46f5bfff ... OK
Starting kernel ...
Booting the kernel fitImage
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
258

## Slide 259
DTO Hands-on 1/2
$ cat fit-image.its
/dts-v1/;
/ {
description = "Linux kernel and FDT blob";
images {
kernel-1 {
description = "Linux kernel";
data = /incbin/("./tmp/deploy/images/qemuarm/zImage");
type = "kernel";
arch = "arm";
os = "linux";
compression = "none";
load = <0x40008000>;
entry = <0x40008000>;
hash-1 {
algo = "crc32";
};
};
fdt-1 {
description = "Flattened Device Tree blob";
data = /incbin/("./qemu.dtb");
type = "flat_dt";
arch = "arm";
compression = "none";
hash-1 {
algo = "md5";
};
};
};
fitImage source format
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
259

## Slide 260
DTO Hands-on 1/2
/ {
[…]
description = "Linux kernel and FDT blob";
images {
Kernel-1 {
...
};
Fdt-1 {
...
};
};
configurations {
default = "conf-1";
conf-1 {
description = "Boot Linux kernel with FDT blob";
kernel = "kernel-1";
fdt = "fdt-1";
hash-1 {
algo = "sha1";
};
};
};
};
fitImage source format
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
260

## Slide 261
DTO Hands-on 1/2
It is possible to bundle multiple
  Kernel images, FDTs, firmwares, bitstreams
  Have multiple configurations
The $fdt_high variable
  Sets the upper bound memory address for FDT relocation
  Special value 0xffffffff = -1 means do not relocate FDT
  Some platforms need FDT close to the kernel binary
Information about uImage and fitImage, “iminfo”
Extracting data from fitImage – “imxtract”
Notes on fitImage
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
261

## Slide 262
DTO Hands-on 1/2
=> iminfo 0x100000
## Checking Image at 00100000 ...
FIT image found
FIT description: Linux kernel and FDT blob
Image 0 (kernel-1)
Description: Linux kernel
Type: Kernel Image
Compression: uncompressed
Data Start: 0x001000ec
Data Size: 5393824 Bytes = 5.1 MiB
Architecture: ARM
OS: Linux
Load Address: 0x40008000
Entry Point: 0x40008000
Hash algo: crc32
Hash value: bf5547fe
Image 1 (fdt-1)
[...]
Default Configuration: 'conf-1'
Configuration 0 (conf-1)
Description: Boot Linux kernel with FDT blob
Kernel: kernel-1
FDT: fdt-1
## Checking hash(es) for FIT Image at 00100000 ...
Hash(es) for Image 0 (kernel-1): crc32+
Notes on fitImage iminfo
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
262

## Slide 263
DTO Hands-on 1/2
=> iminfo 0x100000
## Checking Image at 00100000 ...
FIT image found
FIT description: Linux kernel and FDT blob
Image 0 (kernel-1)
Description: Linux kernel
Type: Kernel Image
[...]
Image 1 (fdt-1)
[...]
Default Configuration: 'conf-1'
Configuration 0 (conf-1)
=> help bootm
bootm - boot application image from memory
Usage:
bootm [addr [arg ...]]
- boot application image stored in memory
...
For the new multi component uImage format (FIT) addresses
must be extended to include component or configuration unit name:
addr:<subimg_uname> - direct component image specification
addr#<conf_uname> - configuration specification
Use iminfo command to get the list of existing component
images and configurations.
Notes on fitImage configurations
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
263

## Slide 264
DTO Hands-on 1/2
OE can generate fitImage using the kernel-bbclass
Add the following entries to your machine config:
Note that it is possible to use multiple DTs
    The fitImage bbclass will generate one fitImage configuration per DT entry
OE kernel-fitimage bbclass
KERNEL_IMAGETYPE = “fitImage”
KERNEL_CLASSES += “kernel-fitimage”
KERNEL_DEVICETREE = “your-machine.dtb”
Notes: ilab01@devday010:/scratch/poky/build-dto$ time bitbake core-image-dto-microdemo
…
real 0m48.756s
user 0m1.336s
sys 0m0.183s
ilab01@devday010:/scratch/poky/build-dto$
ilab01@devday010:/scratch/poky/build-dto$ du -sh tmp/
1.6G tmp/
ilab01@devday010:/scratch/poky/build-dto$
264