## Slide 1
Yocto Project® Kernel Lab, Hands-On
Trevor Woerner, Togán Labs
Yocto Project DevDay Virtual, North America, 2020

## Slide 2
Ignoring TheYocto Project (briefly)
Notes: 2

## Slide 3
Kernel Workflow - first pass
obtain kernel
obtain cross-toolchain
setup cross-toolchain/environment
configure kernel/tweak DT
build kernel/modules/dtb
install kernel/modules/dtb
test

## Slide 4
Kernel Workflow - later
edit kernel
write kernel module
do -rt stuff
build, install, test

## Slide 5
Obtain Kernel
upstream Linus
upstream linux-stable
vendor kernel (tries to be good)
evil vendor kernel (franken-kernel)

## Slide 6
Obtain Cross-Toolchain
cross-compiler from your distro
gnu.gcc.org (compile your own, good luck)
crosstool-NG (compile your own, with help)
ARM/Linaro
Bootlin
kernel.org (NOTE: kernel only)
vendor

## Slide 7
Obtain Cross-Toolchain ARM/Linaro

## Slide 8
Obtain Cross-Toolchain Bootlin - https://toolchains.bootlin.com

## Slide 9
Obtain Cross-Toolchain kernel.org - https://www.kernel.org/pub/tools/crosstool

## Slide 10
Setup Toolchain/Environment
$ export ARCH=arm
$ export CROSS_COMPILE=<toolchain-prefix>
(compile +) install toolchain
setup $PATH
either:
  tweak environment
  specify on cmdline
$ ARCH=arm CROSS_COMPILE=<toolchain-prefix> make

## Slide 11
Setup Toolchain/Environment Configure Kernel
https://asciinema.org/a/344216

## Slide 12
Build Kernel, Modules, DTB
$ ARCH=arm CROSS_COMPILE=<toolchain-prefix> make

## Slide 13
Install Kernel, Modules, DTB
by default:
  kernel: $INSTALL_PATH (default: /boot)
  modules: $INSTALL_MOD_PATH/lib/modules/$VER
  dtb: $INSTALL_PATH/dtbs/$VER
this doesn't work for embedded
  each board is… "unique"

## Slide 14
Install Kernel, Modules, DTB
how and where these various parts are installed is highly board-specific:
  extlinux.conf
  uEnv.txt
  separate partitions
  APPENDED_DTB (i.e. "bundled")
  U-Boot FIT image

## Slide 15
Install Kernel, Modules, DTB
how and where these various parts are installed is highly board-specific:
  "magic" offsets on storage device
  multi-partition UBI (raw flash)
  initial FAT/VFAT partition

## Slide 16
Install Kernel, Modules, DTB
there is a very tight coupling between
  bootloader
  kernel cmdline
  kernel + modules + dtb
  final image assembly (e.g. wic)

## Slide 17
Edit Kernel
not too difficult, locate and edit kernel sources
just make sure you're editing the correct sources (multiple boards, multiple projects, multiple configurations) and using the correct toolchain (correctly)

## Slide 18
Write Kernel Module
need to copy+paste an example Makefile to get the out-of-kernel-tree build plumbing correct
otherwise the mechanics aren't too complicated

## Slide 19
Do -rt Stuff
I hope the kernel version you're using is one for which there is an -rt patch available, otherwise forget it
if the above is true, manually applying the -rt patch against an unmodified base isn't too difficult

## Slide 20
Kernel Workflow Without Yocto
it's not too hard if you've done it once or twice before
but can be tricky to get it right the first time
the amount of work compounds with the number of boards you need to support
  multiple toolchains
  multiple configurations
  multiple install layouts

## Slide 21
Can TheYocto Project Help?
Notes: 21

## Slide 22
Kernel Workflow - multiple users
tweaking a kernel/config or writing a kernel module using an existing BSP
board bring-up (creating a BSP) for a new board

## Slide 23
Kernel Workflow - existing BSP
obtain kernel
obtain cross-toolchain
setup cross-toolchain/environment
configure kernel/tweak DT
build kernel/modules/dtb
install kernel/modules/dtb
DONE!

## Slide 24
Kernel Workflow TODO - existing BSP
change kernel
obtain cross-toolchain
setup cross-toolchain/environment
configure kernel/tweak DT
build kernel/modules/dtb
install kernel/modules/dtb
edit kernel sources
write a kernel module

## Slide 25
Kernel Workflow TODO - existing BSP change kernel
many kernels from which to choose (upstream, vendor, stable)
The Yocto Project provides its own (linux-yocto) plus tooling for use with linux-yocto, or your own
linux-yocto comes in a couple variants:
  (base)
  -dev
  -tiny
  -rt

## Slide 26
use your own defconfig
use an in-kernel _defconfig
generate one or more config "fragments" which are applied on top of the base configuration
Kernel Workflow TODO - existing BSP tweak config

## Slide 27
Kernel Workflow TODO - existing BSP edit kernel code

## Slide 28
Kernel Workflow TODO - existing BSP write a module

## Slide 29
Kernel Workflow - new BSP
obtain kernel
obtain cross-toolchain
setup cross-toolchain/environment
configure kernel/tweak DT
build kernel/modules/dtb
install kernel/modules/dtb
DONE!

## Slide 30
Kernel Workflow - new BSP
obtain kernel
obtain cross-toolchain
setup cross-toolchain/environment
configure kernel/tweak DT
build kernel/modules/dtb
install kernel/modules/dtb
… but with a lot of help!
DONE!

## Slide 31
Kernel Workflow - new BSP
obtain kernel
  implicit understanding of how to fetch code
setup cross-toolchain/environment
  set the processor "TUNE" in $MACHINE
configure kernel/tweak DT
  lots of linux-yocto tooling
install kernel/modules/dtb
  lots of kernel-handling classes

## Slide 32
Hands On: Existing BSP
Notes: 32

## Slide 33
Hands-On: Prep
ilab01:~$ cd scratch
ilab01:~/scratch$ git clone -b dunfell git://git.yoctoproject.org/poky.git
Cloning into 'poky'...
remote: Enumerating objects: 479650, done.
remote: Counting objects: 100% (479650/479650), done.
remote: Compressing objects: 100% (113534/113534), done.
remote: Total 479650 (delta 359015), reused 478925 (delta 358472)
Receiving objects: 100% (479650/479650), 164.40 MiB | 28.37 MiB/s, done.
Resolving deltas: 100% (359015/359015), done.

## Slide 34
Hands-On: Prep
ilab01:~/scratch$ . poky/oe-init-build-env
...
### Shell environment set up for builds. ###
...
ilab01:~/scratch/build$
ilab01:~/scratch/build$ export $PS1="${PS1}lab> "
ilab01:~/scratch/build$ lab>
I like to remind myself this is now a modified-environment shell for builds:

## Slide 35
Hands-On: Prep
ilab01:~/scratch/build$ lab> $EDITOR conf/local
MACHINE = "qemux86-64"
DL_DIR = "/scratch/downloads"
SSTATE_DIR = "/scratch/sstate-cache"
PACKAGE_CLASSES ?= "package_ipk"
SDKMACHINE = "x86_64"
OE_TERMINAL = "screen"
here's what you need to change:

## Slide 36
Hands-On: Prep
ilab01:~/scratch/build$ lab> bitbake core-image-minimal
Build Configuration:
BB_VERSION = "1.46.0"
BUILD_SYS = "x86_64-linux"
NATIVELSBSTRING = "universal"
TARGET_SYS = "x86_64-poky-linux"
MACHINE = "qemux86-64"
DISTRO = "poky"
DISTRO_VERSION = "3.1.1"
TUNE_FEATURES = "m64 core2"
TARGET_FPU = ""
meta
meta-poky
meta-yocto-bsp = "dunfell:93ef4736915090ac9a2402916df8924ac4439490"
baseline build:

## Slide 37
Hands-On: Prep
ilab01:~/scratch/build$ lab> runqemu slirp nographic serial
...
hwclock: settimeofday: Invalid argument
chmod: /var/log/wtmp: No such file or directory
Failed to set mode -0664- for -/var/log/wtmp-.
INIT: Entering runlevel: 5
Configuring network interfaces... ip: RTNETLINK answers: File exists
hwclock: settimeofday: Invalid argument
Starting syslogd/klogd: done
Poky (Yocto Project Reference Distro) 3.1.1 qemux86-64 /dev/ttyS0
qemux86-64 login:
verify it runs

## Slide 38
Hands-On: Prep
Poky (Yocto Project Reference Distro) 3.1.1 qemux86-64 /dev/ttyS0
qemux86-64 login: root
root@qemux86-64:~# uname -a
Linux qemux86-64 5.4.43-yocto-standard #1 SMP PREEMPT Thu May 28 15:33:30 UTC 2020
root@qemux86:~# shutdown -h now
...
[ 130.239174] ACPI: Preparing to enter system sleep state S5
[ 130.242375] reboot: Power down
runqemu - INFO - Cleaning up
ilab01:~/scratch/build$ lab>
shutdown

## Slide 39
Hands-On: Prep
ilab01:~/scratch/build$ lab> bitbake-layers create-layer meta-mytweaks
NOTE: Starting bitbake server...
Add your new layer with 'bitbake-layers add-layer meta-mytweaks'
ilab01:~/scratch/build$ lab> bitbake-layers add-layer meta-mytweaks
NOTE: Starting bitbake server...
ilab01:~/scratch/build$ lab>
create/add a layer for your changes

## Slide 40
Hands-On: Edit the Kernel

## Slide 41
Hands-On: Edit the Kernel
ilab01:~/scratch/build$ lab> devtool modify virtual/kernel
...
Currently 1 running tasks (431 of 437) 98% | ############################ |
0: linux-yocto-5.4.43+gitAUTOINC+aafb8f095e_9e1b13d7f9-r0 do_kernel_checkout - 1m49s (pid 1615575)
INFO: Copying kernel config to srctree
INFO: Source tree extracted to /scratch/build/workspace/sources/linux-yocto
INFO: Recipe linux-yocto now set up to build from /scratch/build/workspace/sources/linux-yocto
use devtool

## Slide 42
Hands-On: Edit the Kernel
ilab01:~/scratch/build$ lab> $EDITOR workspace/sources/linux-yocto/init/main.c
1137 /*
1138 * We try each of these until one succeeds.
1139 *
1140 * The Bourne shell can be used instead of init if we are
1141 * trying to recover a really broken machine.
1142 */
1143 pr_notice("*** --- >>> edit <<< --- ***\n");
1144 if (execute_command) {
1145 ret = run_init_process(execute_command);
1146 if (!ret)
1147 return 0;
1148 panic("Requested init %s failed (error %d).",
1149 execute_command, ret);
edit init/main.c

## Slide 43
Hands-On: Edit the Kernel
ilab01:~/scratch/build$ lab> bitbake core-image-minimal
...
NOTE: linux-yocto: compiling from external source tree /scratch/build/workspace/sources/linux-yocto
...
build

## Slide 44
Hands-On: Edit the Kernel
ilab01:~/scratch/build$ lab> runqemu slirp nographic serial
...
[ 5.209719] VFS: Mounted root (ext4 filesystem) on device 253:0.
[ 5.211596] devtmpfs: mounted
[ 5.312611] Freeing unused kernel image memory: 1580K
[ 5.313286] Write protecting kernel text and read-only data: 20480k
[ 5.313744] *** --- >>> edit <<< --- ***
[ 5.313980] Run /sbin/init as init process
INIT: version booting
Starting udev
[ 6.096177] udevd[138]: starting version 3.2.9
[ 6.162295] udevd[139]: starting eudev-3.2.9
...
test (you might have to scroll up)

## Slide 45
Hands-On: Edit the Kernel
ilab01:~/scratch/build$ lab> pushd workspace/sources/linux-yocto
~/scratch/build/workspace/sources/linux-yocto ~/scratch/build
ilab01:~/scratch/build$ lab> git commit -avs -m "init/main.c: add my tweaks"
ilab01:~/scratch/build$ lab> popd
~/scratch/build
commit your changes

## Slide 46
Hands-On: Edit the Kernel
ilab01:~/scratch/build$ lab> devtool finish linux-yocto meta-mytweaks
...
NOTE: Writing append file /scratch/build/meta-mytweaks/recipes-kernel/linux/linux-yocto_%.bbappend
NOTE: Copying 0001-init-main.c-add-my-tweaks.patch to /scratch/build/meta-mytweaks/recipes-kernel/linux/linux-yocto/0001-init-main.c-add-my-tweaks.patch
INFO: Cleaning sysroot for recipe linux-yocto...
INFO: Leaving source tree /scratch/build/workspace/sources/linux-yocto as-is; if you no longer need it then please delete it manually
ilab01:~/scratch/build$ lab> rm -fr workspace/sources/linux-yocto
update your metadata

## Slide 47
Hands-On: Edit the Kernel
ilab01:~/scratch/build$ lab> tree meta-mytweaks
meta-mytweaks/
├── COPYING.MIT
├── README
├── conf
│ └── layer.conf
└── recipes-kernel
└── linux
├── linux-yocto
│ └── 0001-init-main.c-add-my-tweaks.patch
└── linux-yocto_%.bbappend
check

## Slide 48
Hands-On: Tweak the Kernel Configuration

## Slide 49
Hands-On: Tweak the Kernel Configuration
ilab01:~/scratch/build$ lab> devtool modify virtual/kernel
...
NOTE: Tasks Summary: Attempted 437 tasks of which 426 didn't need to be rerun and all succeeded.
INFO: Copying kernel config to srctree
INFO: Source tree extracted to /z/3.1-build-dunfell/kernellab/x86-64/build/workspace/sources/linux-yocto
INFO: Recipe linux-yocto now set up to build from /z/3.1-build-dunfell/kernellab/x86-64/build/workspace/sources/linux-yocto
use devtool, setup

## Slide 50
Hands-On: Tweak the Kernel Configuration
ilab01:~/scratch/build$ lab> devtool menuconfig linux-yocto
use devtool

## Slide 51
Hands-On: Tweak the Kernel Configuration
navigate to: General Setup Preemption Model
select: No Forced Preemption (Server)
hit double-esc or <Exit> and save your changes
INFO: Updating config fragment /z/3.1-build-dunfell/kernellab/x86-64/build/workspace/sources/linux-yocto/oe-local-files/devtool-fragment.cfg

## Slide 52
Hands-On: Tweak the Kernel Configuration
ilab01:~/scratch/build$ lab> bitbake core-image-minimal
NOTE: linux-yocto: compiling from external source tree /scratch/build/workspace/sources/linux-yocto
ilab01:~/scratch/build$ lab> runqemu slirp nographic serial
...
[ 0.223909] rcu: Hierarchical RCU implementation.
...
qemux86-64 login: root
root@qemux86-64:~# uname -a
Linux qemux86-64 5.4.43-yocto-standard #1 SMP Wed Jul 1 20:06:32 UTC 2020 x86_64 GNU/Linux
test
NOTE: missing "Preemptible hierarchical RCU" and "PREEMPT" in "uname -a"

## Slide 53
Hands-On: Tweak the Kernel Configuration
ilab01:~/scratch/build$ lab> devtool finish linux-yocto meta-mytweaks
...
NOTE: Writing append file /scratch/build/meta-mytweaks/recipes-kernel/linux/linux-yocto_%.bbappend
NOTE: Copying devtool-fragment.cfg to /scratch/build/meta-mytweaks/recipes-kernel/linux/linux-yocto/devtool-fragment.cfg
INFO: Cleaning sysroot for recipe linux-yocto...
INFO: Leaving source tree /scratch/build/workspace/sources/linux-yocto as-is; if you no longer need it then please delete it manually
ilab01:~/scratch/build$ lab> rm -fr workspace/sources/linux-yocto
update metadata

## Slide 54
Hands-On: Tweak the Kernel Configuration
ilab01:~/scratch/build$ lab> tree meta-mytweaks
meta-mytweaks/
├── COPYING.MIT
├── README
├── conf
│ └── layer.conf
└── recipes-kernel
└── linux
├── linux-yocto
│ ├── 0001-init-main.c-add-my-tweaks.patch
│ └── devtool-fragment.cfg
└── linux-yocto_%.bbappend
check

## Slide 55
Hands-On: Tweak the Kernel Configuration
ilab01:~/scratch/build$ lab> cat meta-mytweaks/recipes-kernel/linux/linux-yocto/devtool-fragment.cfg
CONFIG_PREEMPT_NONE=y
# CONFIG_PREEMPT is not set
CONFIG_TREE_RCU=y
CONFIG_INLINE_SPIN_UNLOCK_IRQ=y
CONFIG_INLINE_READ_UNLOCK=y
CONFIG_INLINE_READ_UNLOCK_IRQ=y
CONFIG_INLINE_WRITE_UNLOCK=y
CONFIG_INLINE_WRITE_UNLOCK_IRQ=y
check

## Slide 56
The Yocto Project Kernel Tooling
Notes: 56

## Slide 57
Notes: 57